| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Clarification of HARQ feedback channel index (16.3.9.2.2) |
| Date Submitted | 2009-12-30 |
| Source(s) | Ji-Yun Seol Samsung Electronics | jiyun.seol@samsung.com |
| Re: | IEEE 802.16-09/0073, “IEEE 802.16 Working Group Letter Ballot#30b” Target topic: “IEEE P802.16m/D3 section 16.3.9.2.2 ”. |
| Abstract | The contribution proposes to clarify the HARQ feedback index in Figure 561, which is inconsistent with Table 885. |
| Purpose | To be discussed and adopted by TGm. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Clarification of HARQ feedback channel index (16.3.9.2.2)

Ji-Yun Seol

Samsung Electronics

# Introduction

This contribution proposes clarification on the HARQ feedback channel index in association with the orthogonal sequence index in the current 802.16m draft standard [1].

In Figure 561 illustrating 2x2 HMT structure, the HARQ feedback channel index starts from ‘1’. However, conventionally, the indexing usually starts from ‘0’. Moreover, Table 885 including orthogonal sequences for UL HARQ feedback channel describes the channel index in even/odd manner.

To be consistent and to get rid of potential interoperability issue, it is suggested to modify Figure 561 to specify the HARQ feedback channel index starting from ‘0’ in even-odd order.

# References

[1] IEEE P802.16m/D3, December 2009

# Proposed Text Changes

Blue/Underline: Text Added

Red/Strikeout: Text Deleted

[Change 1: Modify Figure 561 in page 528 as follows]

- - - - - - - - - - - - - - - - - - - - - - - - - - - Begin Proposed Text  - - - - - - - - - - - - - - - - - - - - - - - -

Figure 561—2x2 HMT structure

- - - - - - - - - - - - - - - - - - - - - - - - - - - End Proposed Text - - - - - - - - - - - - - - - - - - - - - - - - -