Report of IEC TC14 Power Transformers

IEEE Transformers Committee Spring Meeting 2014

Savannah 23rd – 27th March 2014

Paul Jarman Chairman TC14

- Last meeting

The last TC14 meeting was held in Milwaukee on 17-18th October 2013, the meeting was particularly successful because of the presence of Don Platts who reported on IEEE work, Jodi Haasz who presented on the Dual Logo procedure and Claude Rajotte who presented on CIGRE A2 work.

- Next Meeting

The next meeting will be held in Tokyo November 10-11 2014 in conjunction with the IEC general meeting at the kind invitation of the Japanese National Committee.

- Website

Attention is drawn to the TC14 website WWW.IEC.CH/TC14 which gives a summary of projects and publications. Attention is also drawn to the website www.electropedia.org which gives a comprehensive electrotechnical vocabulary reference

- New Documents published

- IEC 60076-14 Liquid immersed Power Transformers using high temperature insulation materials

  - Published September 2013

- IEC 60076-19 Rules for the determination of uncertainties in the measurement of losses in power transformers and reactors

  - Published March 2013

  - New technical report based on an existing CENELEC document but significantly revised

  - It is encouraged that this document is used to understand uncertainties in the loss measurement and feedback on its use would be welcomed.

- IEC 60076-3 Insulation levels, dielectric tests and external clearances in air

  - Published July 2013

  - Major revision – document made simpler to use and tests rationalised and clarified.

  - Improved alignment with IEEE

  - Three categories <=72.5kV<=170kV >170kV

  - Change in phase to phase requirement for induced test

  - ‘Line terminal AC’ rather than ACSD

  - Switching impulse levels for all >72.5kV as alternative to LTAC

  - PD for all >72.5kV

  - Induced test levels based on rated rather than max voltage

  - Introduction of K factor in impulse wave

  - Chopped waves routine for >170kV

  - Revised test levels

  - Revised dielectric clearance distances

- New documents in progress

- IEC 60076-20 Energy efficiency for transformers

  - The EU regulation on transformer efficiency was published in January 2014 and is expected to come into force in 2015

  - The first committee draft circulated December 2013 comments closed on 21st March 2014.

  - Reflects 3 world practices for defining energy efficiency

    - Peak Efficiency Index (developed for large transformers)

    - Efficiency at 50%

    - No load and load loss limits

  - Note that following the Milwaukee meeting the two 60076-20 projects for higher and lower voltages have been merged.

- IEC 60076-57-1202 Liquid immersed Phase Shifting Transformers

  - Joint with IEEE – new standard

  - Several meetings held

  - Working towards first committee draft, should be sent to IEC shortly after the Savannah meeting

- IEC 60076-22 Power Transformer and Reactor Fittings as IEC documents

  - 3 parts

    - -1 Protective devices (alarms and trips)

    - -2 Cooling

    - -3 Accessories (passive)

  - Work has started first meeting held in Milan in January 2014.

- Revisions in progress

- IEC 60076-10 Determination of Sound Levels

  - CDV issued November 2013 closed 14th Feb 2014, positive result will now go to final draft for vote.

- IEC 60076-10-1 Determination of transformer and reactor sound levels- User guide

  - First committee draft issued November 2013 closed 14th Feb 2014, now working on CDV in parallel with 60076-10

- IEC 60076-16 Transformers for wind turbine applications

  - Revision of IEC document with IEEE to produce a dual logo

  - Meetings held in London and Savannah

  - Working on first CD

- IEC 61378-3 Converter transformers – Application Guide

  - CDV has now circulated September 2013 closing date for comments was 6th December 2013, positive result (1 negative) now working on final draft.

- IEC 60214-1 Tap changers – performance requirements and test methods

  - Final draft sent to IEC for publication

- IEC 60214-2 Tap changers - Application guide

  - Work has started on the revision and positive comments were received from the document for comment (DC) asking about revision as a dual logo.

- IEC 60076-15 Gas-Filled Power Transformers

  - The CD was circulated (closing date 15th Feb 2013) the CDV has been sent to IEC and will be circulated soon.

- IEC 60076-7 Loading guide for liquid immersed transformers

  - First meetings have taken place the maintenance team is working on the first draft.

- New revisions starting

- IEC  61378-2 HVDC converter transformers

  - Positive response to DC on joint work with IEEE to merge two standards into a dual logo.

  - Meeting held to look at feasibility, positive outcome.

  - Anders Lindroth is convenor for IEC

  - Maintenance team is set up but project not officially started.

- IEC 60076-21 Standard requirements terminology and and test code for step voltage regulators

  - DC asking about dual logo revision with IEEE sent Feb 2014 closing date for comments 9th May 2014

  - Craig Colopy to convene

- IEC 60076-11 Dry-type transformers

  - DC on revision sent out January 2014 closing date for comments 28th March 2014

- IEC 60076-4 Guide to lightning impulse and switching impulse testing – power transformers and reactors

  - Revision agreed in TC14 meeting but no progress to date, Thang Hochanh to convene

- Possible New Documents

- IEEE C57.142 Guide to describe the occurrence and mitigation of switching transients induce by transformer switching device and system interaction

  - This document is referred to in IEC 60076-1 and it may be an advantage to make it dual-logo, NCs to be consulted.