-- 2007/01/23

-- MST Kitchen Sink version 3_0

-- BSDL description of an example 1149.4 device

-- This is an 1149.1-compatible BSDL that encodes 1149.4 features.

-- This remains suitable for use with conventional 1149.1 tools.

-- (such tools may/ will simply ignore the elements that support

--   features pertaining only to 1149.4)

entity Kitchen_Sink_3_0 is

generic (PHYSICAL_PIN_MAP : string := "dip32");

port(

-- TAP pins, as per 1149.1

TCK, TDI, TMS: in bit;

TDO: out bit;

-- ATAP pins, as per 1149.4

-- = required to be inout (bidirectional)

AT1, AT2: inout bit;

-- ATAPN pins, as per 1149.4

-- = only required for optional differential ATAP

-- = required to be inout (bidirectional)

AT1N, AT2N: inout bit;

-- digital pins, as per 1149.1

-- = type/ direction not restricted

A, B: in bit;

-- digital differential pins, as per 1149.1

-- = type/ direction not restricted

D1, D1N: in bit;

D2, D2N: in bit;

D3, D3N: in bit;

D4, D4N: out bit;

D5, D5N: inout bit;

D6, D6N: inout bit;

-- analog pins, as per 1149.4

-- = required to be inout (bidirectional)

W, Y: inout bit;

-- analog differential pins, as per 1149.4

-- = required to be inout (bidirectional)

X1, X1N : inout bit;

X2, X2N : inout bit;

-- linkage pins, as per 1149.1

NC1, NC17: linkage bit;

GND, VCC: linkage bit);

-- standard use statement, as per 1149.1

use STD_1149_1_2001.all; -- Get Std 1149.1-2001 attrs and defns

-- optional use statement, as per 1149.1

-- = standard use statement, as per 1149.4

use STD_1149_4_2007.all; -- Get MST attributes and definitions

-- component conformance, as per 1149.1

attribute COMPONENT_CONFORMANCE of Kitchen_Sink_3_0 : entity is

"STD_1149_1_2001";

attribute PIN_MAP of Kitchen_Sink_3_0 : entity is PHYSICAL_PIN_MAP;

constant dip32 : PIN_MAP_STRING :=

--       -----------

--  NC1  | 1    32 | VCC

--    A  | 2    31 | W

--    B  | 3    30 | Y

--   D1  | 4    29 | X1

--  D1N  | 5    28 | X1N

--  D2N  | 6    27 | X2N

--   D2  | 7    26 | X2

--   D3  | 8    25 | D5

--  D3N  | 9    24 | D5N

--  D4N  | 10   23 | D6N

--   D4  | 11   22 | D6

--  AT1  | 12   21 | AT2

-- AT1N  | 13   20 | AT2N

--  TDI  | 14   19 | TDO

--  TCK  | 15   18 | TMS

--  GND  | 16   17 | NC17

--       -----------

"TCK:15, TDI:14, TMS:18, " &

"TDO:19, " &

"AT1:12, AT2:21, " &

"AT1N:13, AT2N:20, " &

"A:2, B:3, " &

"D1:4, D1N:5, " &

"D2:7, D2N:6, " &

"D3:8, D3N:9, " &

"D4:11, D4N:10, " &

"D5:25, D5N:24, " &

"D6:22, D6N:23, " &

"W:31, Y:30, " &

"X1:29, X1N:28, " &

"X2:26, X2N:27, " &

"NC1:1, NC17:17, " &

"GND:16, VCC:32";

-- grouped port identification, as per 1149.1

-- = required for digital differentials

attribute PORT_GROUPING of Kitchen_Sink_3_0 : entity is

"Differential_Voltage ((D1, D1N)),"&

"Differential_Current ((D2, D2N)),"&

"Differential_Voltage ((D3, D3N)),"&

"Differential_Voltage ((D4, D4N)),"&

"Differential_Voltage ((D5, D5N)),"&

"Differential_Voltage ((D6, D6N))";

attribute TAP_SCAN_CLOCK of TCK : signal is (20.0e6, BOTH);

attribute TAP_SCAN_MODE of TMS : signal is true;

attribute TAP_SCAN_IN of TDI : signal is true;

attribute TAP_SCAN_OUT of TDO : signal is true;

attribute INSTRUCTION_LENGTH of Kitchen_Sink_3_0 : entity is 4;

attribute INSTRUCTION_OPCODE of Kitchen_Sink_3_0 : entity is

-- mandatory instructions, as per 1149.1

"EXTEST  (1000), " &

"PRELOAD (0010), " &

"SAMPLE  (0010), " &

"BYPASS  (0111), " &

-- mandatory instruction, as per 1149.4

-- = opcode may have any value except all ones

-- = opcode value all zeros is not recommended (as per 1149.1)

"PROBE   (1011), " &

-- optional instructions, as per 1149.1

"CLAMP   (0100), " &

"HIGHZ   (1101), " &

"INTEST  (1110), " &

"IDCODE  (0001)";

attribute INSTRUCTION_CAPTURE of Kitchen_Sink_3_0 : entity is "0001";

attribute IDCODE_REGISTER of Kitchen_Sink_3_0 : entity is

"XXXX" &             -- version

"0000000000000000" & -- part number

"10101010101" &      -- manufacturer id

"1";

attribute REGISTER_ACCESS of Kitchen_Sink_3_0 : entity is

-- access to mandatory registers, as per 1149.1

"BOUNDARY (EXTEST, PRELOAD, SAMPLE), " &

"BYPASS (BYPASS), " &

"BOUNDARY (INTEST), " &

-- access to mandatory registers, as per 1149.4

-- = register BOUNDARY must be accessed by instruction PROBE

"BOUNDARY (PROBE), " &

-- access to optional register, as per 1149.1

"DEVICE_ID (IDCODE)";

attribute BOUNDARY_LENGTH of Kitchen_Sink_3_0 : entity is 65;

attribute BOUNDARY_REGISTER of Kitchen_Sink_3_0 : entity is

-- following cells (2) are for the digital pins

-- num cell port function safe [ccell disval rslt]

"0  (BC_1,    A, input,        x), " &

"1  (BC_1,    B, input,        x), " &

-- following cells (13) are for the digital differential pins

-- num cell port function safe [ccell disval rslt]

"2  (BC_4,   D1, observe_only, x), " &

"3  (BC_4,  D1N, observe_only, x), " &

"4  (BC_1,   D1, input,        x), " & -- D1:D1N single-ended

"5  (BC_4,   D2, observe_only, x), " &

"6  (BC_4,  D2N, observe_only, x), " &

"7  (BC_1,   D2, input,        x), " & -- D2:D2N single-ended

"8  (BC_4,   D3, observe_only, x), " &

"9  (BC_4,  D3N, observe_only, x), " &

"10 (BC_1,   D3, input,        x), " & -- D3:D3N single_ended1

"11 (BC_1,   D3, input,        x), " & -- D3:D3N single_ended2

"12 (BC_4,   D4, observe_only, x), " &

"13 (BC_4,  D4N, observe_only, x), " &

"14 (BC_1,   D4, output_2,     x), " & -- D4:D4N driver cell

-- following cells (4) are TBIC base controls

-- num cell port function safe [ccell disval rslt]

"15 (BC_1,    *, internal,     0), " &           -- Ca

"16 (BC_1,    *, control,      0), " &           -- Co

"17 (BC_7,  AT1, bidir,        0, 16, 0, Z), " & -- D1

"18 (BC_7,  AT2, bidir,        0, 16, 0, Z), " & -- D2

-- following cells (2) are TBIC partition controls

-- num cell port function safe

"19 (BC_1,    *, internal,     0), " &           -- D1

"20 (BC_1,    *, internal,     0), " &           -- D2

-- following cells (4) are TBICN base controls

-- num cell port function safe [ccell disval rslt]

"21 (BC_1,    *, internal,     0), " &           -- Ca

"22 (BC_1,    *, control,      0), " &           -- Co

"23 (BC_7, AT1N, bidir,        0, 22, 0, Z), " & -- D1

"24 (BC_7, AT2N, bidir,        0, 22, 0, Z), " & -- D2

-- following cells (2) are TBIC partition controls

-- num cell port function safe

"25 (BC_1,    *, internal,     0), " &           -- D1

"26 (BC_1,    *, internal,     0), " &           -- D2

-- following cells (2) are TBICN partition controls

-- num cell port function safe

"27 (BC_1,    *, internal,     0), " &           -- D1

"28 (BC_1,    *, internal,     0), " &           -- D1

-- following cells (4) control the analog signal W

-- num cell port function safe [ccell disval rslt]

"29 (BC_1,    *, control,      0), " &           -- C

"30 (BC_7,    W, bidir,        x, 29, 0, Z), " & -- D

"31 (BC_1,    *, internal,     0), " &           -- B1

"32 (BC_1,    *, internal,     0), " &           -- B2

-- following cells (4) control the analog signal Y

-- num cell port function safe [ccell disval rslt]

"33 (BC_1,    *, control,      0), " &           -- C

"34 (BC_7,    Y, bidir,        x, 33, 0, Z), " & -- D

"35 (BC_1,    *, internal,     0), " &           -- B1

"36 (BC_1,    *, internal,     0), " &           -- B2

-- following cells (4) control the analog differential signal X1

-- num cell port function safe [ccell disval rslt]

"37 (BC_1,    *, control,      0), " &           -- C

"38 (BC_7,   X1, bidir,        x, 37, 0, Z), " & -- D

"39 (BC_1,    *, internal,     0), " &           -- B1

"40 (BC_1,    *, internal,     0), " &           -- B2

-- following cells (4) control the analog differential signal X1N

-- num cell port function safe [ccell disval rslt]

"41 (BC_1,    *, control,      0), " &           -- C

"42 (BC_7,  X1N, bidir,        x, 41, 0, Z), " & -- D

"43 (BC_1,    *, internal,     0), " &           -- B1

"44 (BC_1,    *, internal,     0), " &           -- B2

-- following cells (4) control the analog differential signal X2

-- num cell port function safe [ccell disval rslt]

"45 (BC_1,    *, control,      0), " &           -- C

"46 (BC_7,   X2, bidir,        x, 45, 0, Z), " & -- D

"47 (BC_1,    *, internal,     0), " &           -- B1

"48 (BC_1,    *, internal,     0), " &           -- B2

-- following cells (4) control the analog differential signal X2N

-- num cell port function safe [ccell disval rslt]

"49 (BC_1,    *, control,      0), " &           -- C

"50 (BC_7,  X2N, bidir,        x, 50, 0, Z), " & -- D

"51 (BC_1,    *, internal,     0), " &           -- B1

"52 (BC_1,    *, internal,     0), " &           -- B2

-- following cells (11) are for the digital bidirectional differential pins

-- num cell port function safe [ccell disval rslt]

"53 (BC_4,   D5, observe_only, x), " &

"54 (BC_4,  D5N, observe_only, x), " &

"55 (BC_1,   D5, input,        x), " & -- D5:D5N single-ended

"56 (BC_1,    *, control,      0), " & -- controls output enable

"57 (BC_7,   D5, output_3,     x, 56, 0, Z), " & -- D5:D5N driver cell

"58 (BC_4,   D6, observe_only, x), " &

"59 (BC_4,  D6N, observe_only, x), " &

"60 (BC_1,   D6, input,        x), " & -- D6:D6N single-ended1

"61 (BC_1,   D6, input,        x), " & -- D6:D6N single-ended2

"62 (BC_1,    *, control,      0), " & -- controls output enable

"63 (BC_7,   D6, output_3,     x, 62, 0, Z), " & -- D6:D6N driver cell

-- following cell  (1) is a "dummy"

"64 (BC_1,    *, internal,     0)";

-- BSDL extensions follow, as per 1149.1

-- MST attributes declared in package "Std_1149_4_2007", as per 1149.4

-- component conformance, as per 1149.4

attribute MST_COMPONENT_CONFORMANCE of Kitchen_Sink_3_0 : entity is

"STD_1149_4_1999";

-- ATAP port identification, as per 1149.4

-- MST ATAP Identification

attribute MST_AT1  of Kitchen_Sink_3_0 : entity is "AT1";

attribute MST_AT2  of Kitchen_Sink_3_0 : entity is "AT2";

-- ATAPN port identification, as per 1149.4

-- MST ATAP Identification

-- = only required for optional differential ATAP

attribute MST_AT1N of Kitchen_Sink_3_0 : entity is "AT1N";

attribute MST_AT2N of Kitchen_Sink_3_0 : entity is "AT2N";

-- MST test bus TBIC statement, as per 1149.4

attribute MST_TestBus_TBIC of Kitchen_Sink_3_0 : entity is

" AT1,   AT2 : " &  -- pin1, pin2

" 15,     16   " &  -- Ca_num, Co_num

-- partition_name D1_num D2_num

"( BASE   (17, 18), " &

"  PART1  (19, 20), " &

"  PART2  (25, 26) )" &

" AT1N,  AT2N : " &  -- pin1, pin2

" 21,    22     " &  -- Ca_num, Co_num

-- Npartition_name D1_num D2_num

"( BASEN  (23, 24), " &

"  PART1N (27, 28)) " ;

-- MST ABM statement, as per 1149.4

attribute MST_ABM of Kitchen_Sink_3_0 : entity is

-- ABMs, as per 1149.4 = ref tables 6, 7, and 8

-- port partition_name C_num D_num B1_num B2_num

"W   ( BASE  : 29, 30, 31, 32 ), " &

"Y   ( BASE  : 33, 34, 35, 36 ), " &

"X1  ( PART1 : 37, 38, 39, 40 ), " &

"X1N ( BASEN : 41, 42, 43, 44 ), " &

"X2  ( PART2 : 45, 46, 47, 48 ), " &

"X2N ( PART1N: 49, 50, 51, 52 )";

-- MST differential statement, as per 1149.4

attribute MST_PORT_GROUPING of Kitchen_Sink_3_0 : entity is

"Differential_Digital ( " &

"((D1, D1N) :  4)," & -- cell 4 captures D1 value

"((D2, D2N) :  7)," & -- cell 7 captures D2 value

"((D3, D3N) :  10, 11), " & -- cells 10 and 11 capture D3 value

"((D5, D5N) :  55)," & -- cell 55 captures D5 value

"((D6, D6N) :  60, 61)), " & -- cells 60 and 61 capture D6 value

"Differential_Analog ( " &

"((X1, X1N) : 39), " &

-- cell 39 captures digitized voltage difference between X1 and X1N

"((X2, X2N) : 47))" ;

-- cell 47 captures digitized voltage difference between X2 and X2N

-- For analog capture cell, refer 7.4.1.1h and i.

end Kitchen_Sink_3_0;