Change-tracking markup shows ALey edits as of 26 Apr 2006:

= note that my edits are based on and made to accommodate the primary assumption that the scope of section 13 and the purpose of section 14 should be incorporated verbatim in like-named sections of clause 1 in the final approved standard and, as such, considering that this project is a revision, must incorporate the scope of the original standard as well as the proposed modification.

= note that my proposals below base the scope and purpose of the original standard on the scope and purpose statements of the 2001 PAR (now expired) and on the abstract, introduction, and scope of the standard sections of the approved IEEE Std 1149.4-1999.

= please note that it certainly won’t hurt my feelings if someone else thinks this needs further word-smithing… I’m quite certain that it does, but I’ve looked at it for so long now that I can’t see the sentences for the words as they might say…

Section 13 – Scope of proposed project.

This project defines a mixed-signal test bus architecture that provides the means of control of and access to both analog and digital test data such that the testability structure for digital circuits described in IEEE Std 1149.1-2001 has been extended effectively to provide similar facilities for mixed-signal circuits. In addition to testing of interconnections in the conventional sense of IEEE 1149.1-2001, the mixed-signal test bus defined by this project also provides the means for parametric testing and, optionally, the means to access internal test structures. The project does not mandate implementation details of the test circuitry, although examples of conformant implementations are given for illustration.

Further, the project develops extensions to Boundary-Scan Description Language (BSDL) as a means of describing key aspects of the implementation of this project within a particular component. At present, this project specifically omits the description of any and all analog parameters defined by the project.

Section 14 – Purpose of proposed project.

Where the standardized structures defined by this project are incorporated into mixed-signal circuits, the testability problems posed by such circuits are mitigated by way of improving the controllability and observability of mixed-signal designs and supporting mixed-signal built-in test structures in order to reduce both test development time and testing costs and to improve test quality. In particular, these standardized test features allow mixed-signal (analog and/ or digital) electronic components, printed circuit assemblies, and electronic systems to be accessible to external or built-in test equipment for interconnect test, parametric test, and internal test.

A further purpose of this project is to define the descriptive elements of BSDL and specified extensions sufficient to support the development of automated test algorithms used for testing interconnections between devices that adhere to this project and, where practical, between such devices intermixed with devices that incorporate IEEE Std 1149.1-2001 or IEEE Std 1149.6-2003 as well. The descriptive elements defined by this project also largely support the automated construction of analog tests for external components attached to or between components that implement this project with the caveat that such tests may subsequently require modification to account for undocumented analog features within the conformant components.

Section 15 – Reason for the proposed project.

The reason for this project, as a revision to an existing approved standard, primarily is to support the development of software that can quickly create automatically generated tests to perform interconnection and parametric tests using the mixed-signal test bus architecture defined by this standard.

A further need for other editorial changes and minor corrections has been identified over the course of use to date of the project. A particular focus of such revisions will focus on harmonization with IEEE Std 1149.1-2001.

21. Additional explanatory notes (item number and explanation)

= note, per NesCom conventions, all PARs for the revision of a standard shall include an indication of all changes being made to the standard under "Additional Explanatory Notes" of the PAR form.

= can we get at least a general overview of the “editorial and minor corrections” that Mr. Cron intends to make?