## Slide 1: Gates vs. Windows and Scheduled Traffic
Christian Boiger
christian.boiger@hdu-deggendorf.de
IEEE 802.1 Interim
January 2013
Vancouver, Canada

## Slide 2
Terminology “Scheduled Traffic”

## Slide 3: Terminology
What is Scheduled Traffic?
To call everything scheduled is on the one hand correct, but people might think they have to engineer / schedule their best effort traffic
In reality the “schedule for best effort” is a consequence of the schedule for the Scheduled Traffic
802.1 Qbv PAR:
“Virtual Local Area Network (VLAN) tag encoded priority values are allocated allowing simultaneous support of scheduled traffic, credit-based shaper traffic and other bridged traffic over Local Area Networks (LANs).”

## Slide 4: Terminology
I think we should stick to Best Effort, Reserved and Scheduled Traffic
What does Scheduled Traffic distinguish from other traffic?
  It is scheduled in the end station on a per stream basis
  It has the highest priority/priorities
  It is registered in bridges (domain concept, priority regeneration, no flooding, …)
How do we call the TSN traffic in general?

## Slide 5: Possible Solution
Time Sensitive Traffic
Reserved Traffic
Scheduled Traffic
Best Effort Traffic

## Slide 6
Gates and Transmission Windows

## Slide 7: Background
In Santa Cruz we had a discussion about alternative ways to configure the Time Aware Shaper
 Configuration of the Scheduled Traffic windows instead of the configuration of the gates in order to allow a floating guard band

## Slide 8: Impacts on the Time Aware Shaper
The general question is:
What should be configured? Gates or transmission windows?

## Slide 9: Configuring Gates
Configuring gates is complicated in combination with an intelligent guard band usage (i.e. transmitting lower priority frames during the guard band if they end before the start of the Scheduled Traffic transmission)
If the gate events are defined as the points in time when the queues are getting (dis)connected from/to the transmission selection it is not possible to transfer frames during the guard band

## Slide 10: How it is specified in IEEE 802.1Qbv-D0.2
“… frames are selected from the corresponding queue for transmission if and only if
…
b) The transmission gate (8.6.8.4) associated with that queue is in the open state; and
c) If there are gate events associated with that queue, then there is sufficient time available to transmit the entirety of that frame before the next gate-close event associated with that queue;”

## Slide 11: Implications of the Current Definition
The gate-closing event is not really defining the time when the queue is disconnected from the transmission selection
It is not possible to start the transmission of a scheduled traffic frame when the corresponding gate is in the open state, if it is not possible to transmit the frame until the closing event
The idea to open the gate only a very short time in order to reschedule the traffic is not possible anymore
But now it is possible to reschedule the frames with the gate-closing events
The usage of the term gates in D0.2 is not really compatible with the definition of gates, it seems to be the definition of transmission windows
Should we change the name?

## Slide 12: IEEE 802.1Qbv D0.1
The example (slide 8) with the D0.2 shaper would look like this:
The queues get disconnected before the gate-closing event, the exact time depends on the frame size of the frames in the other queues.
The gates define now the transmission windows rather than the connection or disconnection from the transmission selection

## Slide 13: Pros and Cons of the IEEE 802.1Qbv D0.2 Shaper
Pros:
Not necessary to define a guard band
Flexible configuration
Gate-closing event allows to reschedule the traffic
Cons:
If the scheduled traffic windows are smaller than a max frame (this might be the usual case) and a frame bigger than the transmission window enters the queue (a talker sends a too big frame (fault)) the queue is blocked (“for ever”)

## Slide 14: Time Aware Shaper – Gate Model

## Slide 15: Time Aware Shaper – Window Model

## Slide 16: Event List
One list per queue
Events:
  Gate events:
  Window close event = 0
  Window open event = 1
  Other events:
  Repeat
Gate event time interval (T0, T1, …, Tx)
  Relative to last gate event
  Granularity: 1ns
  32 bit unsigned integer in units of 1 ns (max ≈ 4.2s)
  In order to have a defined start condition at tR, T0 must be 0
  tR = PTP epoch

## Slide 17: Important Device Specific Parameters
Device specific latency t_Device
 Necessary to calculate the schedule
Device specific Time Aware Shaper granularity
 Necessary to define the minimum window size
Maximum event list length

## Slide 18: End Station – Talker
Shaping in the end stations
 Per stream shaping in the end stations
 Less complicated than CBS
 Ensures that a frame from the scheduled stream is transmitted

## Slide 19: End Station – Talker

## Slide 20
Traffic Class and PCP

## Slide 21: Time Aware Domain and Class
Time Aware (TA) domain
Time Aware (TA) class
time aware (TA) class:
A traffic class whose frames are scheduled in order to achieve minimum latency. A priority value is associated with each TA class. TA classes are denoted by consecutive letters of the alphabet, starting with A and continuing for up to seven classes.
New PCP for Scheduled Traffic: 4 (default for TA class A)
Scheduled Traffic has the highest priority (above AVB Gen1 SR class A)

## Slide 22: Thank You