## Slide 1
Summary: La Jolla MAC Layer Discussions

## Slide 2
La Jolla Questions about WPAN
Can a proper subset of 802.11 MAC be used for PAN?
Can a subset of the 802.11 MAC lead to a significant implementation simplification and power consumption reduction?
By what means and by how much can the MAC be simplified? What ratio of cost reduction might be expected?
What incremental benefit can be derived from simplifying the RF (PHY) relative to the MAC?

## Slide 3
Commentary on MAC
Best way to coexist with 802.11 is to reuse 802.11.
Power savings “could” be accomplished by selecting a subset of options from those available in 802.11 and then hard wiring those options.
Ad hoc and AP complexity are comparable.
Ad hoc still requires ATIM
Authentication and WEP are significant contributors to MAC complexity.
Chris Zegelin foresees single RF and single MAC devices.
Master slave - is the lowest power arrangement

## Slide 4
MAC Commentary (Cont.)
Removing AP function would greatly simplify MAC - but adds complexity every where else.
Device MAC could be simplified to talk to ad hoc only
How does association work in ad hoc network.
Temporary access point assignment to reduce power consumption.
Current MAC is not optimized for low power - there are better ones.
Network coalescing adds great complexity which should be concentrated in AP.

## Slide 5
Review of the 802.11 MAC
What option set of the 802.11 MAC would be appropriate for WPAN?

## Slide 6
Options to KEEP
Single BSS
Peer to peer data frame type
IBSS Beacon/join

## Slide 7
Options to EXTEND
Add a new power management protocol

## Slide 8
Options to REMOVE or make OPTIONAL
Reduces real time computational load
MIB
PCF
RTS/CTS
Fragmentation
NAV
WEP
Association/authentication
TIM/DTIM
Multiple rates
ESSID
to DS / from DS
Wireless DS