## Slide 1
Impact of Bluetooth on 802.11 Direct Sequence Wireless LANs
Greg Ennis
Ennis Associates
16331 Englewood Ave.
Los Gatos, CA 95032

## Slide 2
Fast Frequency Hopping
Bluetooth is a fast frequency hopping system focused on PAN applications
  basic hopping period 625 microseconds
Supports voice and data
Low power with higher power option
No carrier sense, no deferral
Operates within 2.4 GHz band

## Slide 3
Bluetooth/802.11 Environment

## Slide 4
Bluetooth-induced collisions

## Slide 5
Overlap Probability
What is the probability that an 802.11 packet and a Bluetooth transmission will overlap in both time and frequency?
Time overlap: depends on duration of packet and relative timing of BT hopping
Frequency overlap: depends upon number of channels - geographic dependence

## Slide 6
Time Overlap
Let L = 802.11 packet duration, H = Bluetooth dwell duration
Packet will partially overlap either ⎡L/H⎤ or
⎡L/H⎤ + 1 dwell periods, depending on relative timing
Here ⎡x⎤ = ceiling(x) = least integer greater than or equal to x

## Slide 7
Example Time Overlap
Suppose d = the "delta" between the last Bluetooth hop and the start of the packet, where L = 1.3H and d > .7H
Then the packet will overlap 3 Bluetooth dwell periods

## Slide 8
Time Overlap Probability
The probability that an 802.11 packet of duration L will overlap with ⎡L/H⎤ Bluetooth dwell periods of duration H is
⎡L/H⎤ - L/H
The probability that it overlaps with ⎡L/H⎤ + 1 dwell periods is
1 - ⎡L/H⎤ + L/H

## Slide 9
Frequency Overlap
In North America, the probability that at any given time a Bluetooth transmitter is on a narrowband channel outside of a given wideband 802.11 DS channel is 2/3
If an 802.11 packet overlaps with N Bluetooth dwell periods, the probability of no frequency overlap is (2/3)N

## Slide 10
Combining Time and Frequency Overlap Probabilities
For North American operation, the probability that an 802.11 packet of duration L experiences no Bluetooth collisions is
(2/3)⎡L/H⎤ (⎡L/H⎤ - L/H)
+ (2/3)(⎡L/H⎤+1) (1 - ⎡L/H⎤ + L/H)

## Slide 11
What 802.11 Mechanisms to use?
Fall back rates
  increases packet size, hence likelihood of error
RTS/CTS
  Bluetooth won’t obey. RTS/CTS may succeed yet DATA transfer fails
Reassociation to a new AP
  Same interference will be present
Fragmentation

## Slide 12
Fragmentation
802.11 MAC allows for fragmentation
Chain of frames DATA-ACK-DATA-ACK, separated by SIFS
In case of error, transmitter backs off, continues starting with errored fragment
Overhead: PHY and MAC headers
Beneficial under high error conditions

## Slide 13
Model of Bluetooth/802.11 DS
Model developed incorporating calculation on overlap probability
Inputs: 802 Data rate + packet size, Bluetooth hop rate + picocell utilization
Output: “Degradation Factor” versus fragment size
  Degradation Factor is ratio of nonfragmented unimpaired transmission time to impaired time

## Slide 14
Example at 5.5. Mb/s

## Slide 15
Various BT picocell utilizations

## Slide 16
11 Mb/s Situation

## Slide 17
2 Mb/s, 500 byte packet

## Slide 18
Limited Bandwidth Situations
France, Japan, etc.
Impact is even more significant
Example: if only two 802.11 channels available, expression for non-collision becomes
(1/2)⎡L/H⎤ (⎡L/H⎤ - L/H)
+ (1/2)(⎡L/H⎤+1) (1 - ⎡L/H⎤ + L/H)

## Slide 19
2 Versus 3 Channels

## Slide 20
Conclusions
Bluetooth can impact 802.11 DS significantly, particularly on large packets
Most 802.11 mechanisms for responding to poor channel quality either have no impact or make things worse
Fragmentation can help, mainly at lower data rates and high picocell utilizations
Fallback to low-rate FH may be useful