## Slide 1: Improved Coexistence in the HS Standard
By Jan Boer
Lucent Technologies
and
Mark Webster
Harris Semiconductor

## Slide 2: The problem: Long/Short preamble coexistence
Station not supporting the short preamble option and station using short preamble at transmit are not coexistent
Standard ‘prescribes’ to use only the short preamble, when all stations are capable of processing it
  All stations in BSS, ESS ?
  What about different co-located networks
    how do you know ?
    does a neighboring network force you to use the long preamble ?
  Prescription raises many questions; no real solution for coexistence issue

## Slide 3: Long/Short issue
Transmitter using short preamble
Station 2
-waiting to transmit
-not capable to process short preamble
- CCA mode 2 or 3 (carrier sense): CCK is not recognized as carrier
Short preamble
CCK or PBCC
CCK or PBCC
Carrier sense (CCA busy)
Carrier drops (CCA idle)
COLLISION
(near 100%)
Station 1
Notes: The main problem is in the case where a PPDU with a short preamble is being transmitted, while a transceiver configured to receive a long preamble only, wants to transmit. Suppose the transceiver is also configured in CCA mode 2 or 3 (carrier or carrier above energy level).
The receiver will sense the carrier of the short preamble, set CCA busy and waits for the longSFD. The SFD will not be detected. After the short preamble a CCK modulated signal is in the air. The receiver returns to the idle state (no SDF or drop of carrier) and senses the medium before transmitting the waiting frame. There is no carrier sense because of the CCK modulated signal (CCA idle). A transmission will start resulting in a collision. The chance on a collision in this scenario is 100%!

## Slide 4: Related issue
  When the CRC check fails or the carrier drops before validation of the header the exact same issue occurs, indifferent on a short or long preamble!
  The receiving station goes to the idle state and subsequently will sense the medium idle (no carrier detect on the CCK or PBCC part (MPDU))
  Again chance on a collision!

## Slide 5: The resolution
  Keep CCA busy during the transmission of the CCK frame
  HOW?
Short preamble
CCK
CCK
Carrier sense (CCA busy)
Carrier drops
Station 1
Station 2
KEEP CCA BUSY
Notes: Provisions have to be added to cope with this, otherwise the standard is broken. It must be guaranteed that CCA stays busy during reception of (until the end of) the CCK signal.

## Slide 6: IEEE802.11-1997 CCA MODES
CCA MODE 1
Detects Signals with Sufficient Energy
Cannot Discriminate Different Signal Types
Fails to detect very weak 1 and 2 Mbps signals
MEASURE
STRENGTH
Receive
Signal
+
-
Energy
Detect
ED
Threshold
RSSI

## Slide 7
IEEE802.11-1997 CCA MODES
MEASURE
STRENGTH
+
-
Carrier
Sense
CS
Threshold
BARKER
CORR
Receive
Signal
CCA MODE 2
Detects Signal Containing BARKER Codes
Ignores Other Signal Types
Fails on CCK and PBCC

## Slide 8
CCA MODE 3
Detect Only the Signals with Both Sufficient Energy and Containing Barker Codes
Fails on CCK and PBCC
Fails to detect very weak 1 and 2 Mbps signals
IEEE802.11-1997 CCA MODES
MEASURE
STRENGTH
Receive
Signal
+
-
Energy
Detect
ED
Threshold
MEASURE
STRENGTH
+
-
Carrier
Sense
CS
Threshold
BARKER
CORR
Energy Detect
and Carrier
Sense
RSSI

## Slide 9
VIRTUAL CCA OPERATION
IEEE802.11-1997 CCA MODES
PREAMBLE
HEADER
MPDU (Data)
LONG PREAMBLE
SIGNAL
SERVICE
LENGTH
CRC
If CRC failure does not occur, the packet length is known
A known packet length is used to hold-off CCA

## Slide 10
PROBLEMS WITH EXISTING CCA MODES
PREAMBLE
HEADER
MPDU (Data)
PREAMBLE
HEADER
MPDU (Data)
LONG PREAMBLE
SHORT PREAMBLE
IEEE802.11--1997 Requires CCA 1 or CCA2 or CCA 3
5.5 or 11 Mbps MPDU (Data) is Not Recognized by CCA2 or CCA3
Virtual CCA fails if Header CRC Error Occurs
IEEE802.11--1997 Requires CCA 1 or CCA2 or CCA 3
5.5 or 11 Mbps MPDU (Data) is Not Recognized by CCA2 or CCA3
Virtual CCA fails since short preamble is only an option

## Slide 11
DOES ANY CCA TECHNIQUE NOT FAIL, IF USED? -- YES
SUCCESSFUL CCA METHOD #1
Same as TGa CCA
Ignores Carrier Sense
Detects Signals with Sufficient Energy
Cannot Discriminate Signal Types
CCA Inhibited by Strong Interference
Fails to detect very weak 1 and 2 Mbps signals
CCA
TRUE
CCA
DEFER
RSSI Above
Threshold
RSSI Below
Threshold
MEASURE
STRENGTH
Receive
Signal
+
-
Energy
Detect
ED
Threshold
RSSI

## Slide 12
SUCCESSFUL CCA METHOD #2
Initiated by Carrier Sense (legacy CCA Mode 2)
Drops on RSSI-low (legacy CCA Mode 1) or Timer Expiration (New)
Detects Signals with Sufficient Energy
Identifies BARKER-Code Based Signal Types
Not Inhibited by Strong Interference
Fails to drop CCA defer on very weak 1 and 2 Mbps signals
DOES ANY CCA TECHNIQUE NOT FAIL, IF USED? -- YES
CCA
TRUE
CCA
DEFER
Carrier
Sense
RSSI Below Threshold
or Timer Expires

## Slide 13
SUCCESSFUL CCA METHOD #3
Initiated by Carrier Sense and RSSI High (legacy CCA Mode 3)
Drops on RSSI-low (legacy CCA Mode 1) or Timer Expiration (New)
Detects Signals with Sufficient Energy and BARKER Codes
Not Inhibited by Strong Interference
Fails to detect very weak 1 and 2 Mbps signals
DOES ANY CCA TECHNIQUE NOT FAIL, IF USED? -- YES
CCA
TRUE
CCA
DEFER
Carrier Sense
and RSSI Above
Threshold
RSSI Below Threshold
or Timer Expires

## Slide 14
SUCCESSFUL CCA METHOD #4
Initiated by Carrier Sense and RSSI High (legacy CCA Mode 3)
Drops on RSSI-low (legacy CCA Mode 1) or Timer Expiration (New)
Detects Signals with Sufficient Energy and BARKER Codes
Not Inhibited by Strong Interference
Successfully detects very weak 1 and 2 Mbps signals
DOES ANY CCA TECHNIQUE NOT FAIL, IF USED? -- YES
CCA
TRUE
CCA
DEFER
Carrier Sense
and RSSI Above
Threshold
RSSI
Below
Threshold
or Timer Expires
CCA
DEFER
Carrier Sense
and RSSI Below
Threshold
CS Drops
or Timer
Expires

## Slide 15: Proposal
  It is proposed to replace the legacy CCA modes by the improved modes (modes 1,3 and 4; mode 2=mode 3)
  Mode used and threshold settings is the implementers choice; thresholds are not required to be fixed
    depending on network configuration/topology
      cell size, distance, throughput
  It is proposed to maintain the minimal requirements for the thresholds of IEEE 802.11-1997
  Conformance will be demonstrated by also applying a HR/DSSS signal with short preamble
    requirement: CCA stays busy during the whole frame

## Slide 16: Watchdog timer
When CCA mode 1 is forced in a interfered environment CCA will remain busy also after the DSSS (CCK or PBCC) signal
Therefor a watchdog timer is proposed to overcome this situation. When the timer is expired the CCA mode will go back to its original state.
The timer is set to the longest anticipated frame (2400 bytes @ 1 Mbit/s = 19.5 ms
Preamble
CCK
Station 1
Interferer
Station 2
CCA mode 1,2,3 or 4
CCA mode 1,2,3 or 4
CCA mode 1
Watchdog timer

## Slide 17
REMAINING PROBLEM : LEGACY SYSTEMS
TGb PAR was contingent on not changing 1 and 2 Mbps DSSS standard
TGb PAR was contingent on not changing MAC
Hence, cannot impose any Successful CCA Method on legacy systems
Legacy systems can never be forced to CCA on either CCK, PBCC or short preamble
What is solution to dilemma?
DILEMMA
5.5 and 11 Mbps
1 and 2 Mbps
High-Rate Modes
Built Upon
Legacy
Low-Rate Modes
PAR VIEWPOINT
Legacy DSSS
(IEEE802.11-1997)

## Slide 18
PROPOSED ALTERNATIVE PAR VIEWPOINT
1 and 2 Mbps
5.5 and 11 Mbps
1 and 2 Mbps
FOUR RATE SYSTEM
TWO RATE SYSTEM
1 and 2 Mbps DSSS only
IEEE802.11-1997
In the future, two-rate sytems would still be developed only to IEEE802.11-1997
It is recommended to
implement Improved CCA
(not in conflict with legacy
CCA)
1, 2, 5.5 and 11 Mbps implementations
1, 2, 5.5 and 11 Mbps Bound Together
With Improved CCA
Four-rate systems now fully coexistent
Two-rate systems will eventually be phased out in the market place
Two-rate systems only causes problems with long-preamble if CRC error occurs
Bound Together With
Improved CCA

## Slide 19: Additional Short option requirement
It should not be the network operators or users concern whether a station, capable of receiving a short preamble, is receiving a frame with a short or long preamble
It should be required that a station
  with the short preamble option implemented
  configured to send only long preambles
AUTODETECTS a short preamble