## Slide 1: Non Rectangular Time Windowing Analysis for IEEE 802.11 OFDM System
Bob Ward in Cooperation with Symbol Technologies, Inc.

## Slide 2: Introduction
This contribution examines the potential error caused by the non-rectangular window included in the OFDM standard.
It is observed that phase rotation and spreading of the constellation points results after ideal demodulation.
This error can impact synchronization, modulation error measurements and data decoding unless mitigated.

## Slide 3: Short Training Signal Windowed
Draft Standard’s defining equations includes windowing
A transition time, defined as Ttr, is said to be “about” 100 nsec. In fact, earlier draft versions, imply relationship to the rolloff parameter of the raised cosine window.
  The rolloff parameter,, can be related to two FFT samples. With respect to the 4 sec OFDM symbol,
    Letting  = 2/64 indicates that T = 100 nsec exactly, where T = 3.2 sec, is the active symbol duration.

## Slide 4: Windowed vs Ideal Short Symbol
Applying the window transition causes dispersion from the ideal rectangular time window, after ideal demodulation.
  Single 16 point short symbol
  Error from ideal approximately, -22.8 db (following standard’s MER equation)
  Tshort length commensurate with short symbol length

## Slide 5: Windowed Long training Symbol with GI
Long training symbol windowed shows less dispersion
  since impact of non unity multiplication applies to relatively less of the signal
  80 symbols long + windowing
  Long training symbol can be viewed as a QPSK data symbol
  Error approximately -25.4 db

## Slide 6: Observations
Greater effect on shorter symbols
Above examples are for QPSK
  Impact anticipated to be greater for more dense constellations
Error
  Can bias synchronization estimates
  Close to modulation error requirements of -18 or -21 db for QPSK and potentially make them not realizable

## Slide 7: Recommendation
Current references to windowing in the standard are described as informative only and used for convenience
  The convenience is not necessary as appending time intervals over which a definition is valid is the usual format
Remove references to current time windowing. Benefits include
  Allows for closer alignment with BRAN
  Eliminates confusion
  Avoids potential for signal degradation due to this cause.