## Slide 1
NPRM 99-149 Study Group Update
WBFH - Jim Zyren
DS Processing Gain - Al Petrick

## Slide 2
Federal Communications Commission
NPRM: NOTICE OF PROPOSED RULE MAKING
Amendment of Regulations for Part 15 Spread Spectrum Devices
ET Docket No. 99-231 FCC 99-149
Released: June 24, 1999
Comment Date: [75 days after publication in the Federal Register]
Reply Comment Date: [105 days after publication in the Federal Register]
FCC proposes to amend the Part 15 Section 247 rules regarding the operation of ISM spread spectrum systems.
Frequency hopping systems operating in the 2.4 GHz band (2400 - 2483.5 MHz) to allow for wider operational bandwidths.
Refine the method for measuring the processing gain of direct sequence systems.
Goal: Facilitate development and deployment of spread spectrum technology, particularly for high data rate wireless applications.

## Slide 3
Summary of WBFH Proposals

## Slide 4
Tuesday Evening WBFH Summary

## Slide 5: Motion
The study group to draft a letter on behalf of 802.11 in opposition of WBFH as defined in NPRM 99-231. This document after approval of 802.11 plenary will be forwarded to ExCom for approval for release to the FCC.

## Slide 6
Processing gain (PG) shall be > 10dB
PG = improvement in SNR after filtering from coding and spreading
Today: PG (dB) = SNR with spread on
SNR with spread off
Proposed Methods:
No changes If chip rate > 10 chips/symbol
If chip rate < 10 chips/symbol
Traditional CW jammer test
    AND
    Mathematical calculation of processing gain
OR
Jamming margin test using Gaussian Noise
DS Processing Gain

## Slide 7
Tuesday Evening DS Processing Gain Summary

## Slide 8: Motion
802.11 plenary adopts the recommendation as stated in the summary on slide 7 of doc 99/162.