## Slide 1: Critics of IEEE P802.11 response to FCC NPRM 99-149
Naftali Chayat
BreezeCOM
naftalic@breezecom.co.il

## Slide 2: IEEE802.11 response to NPRM 99-149
The response in document P802.11-99/162 tries to protect the 802.11 investment, which is OK.
The 802.11 response contains speculative arguments which are inappropriate for IEEE sponsored response.
The response blocks new innovative uses of the ISM band.
The response fails to address the potential benefit of wider channels to WPAN

## Slide 3: The FCC NPRM 99-149 in a nutshell
To allow FH with channels which are either
  3 MHz wide, allowed power reduced from 1 W to 330 mW
  5 MHz wide, allowed power reduced from 1 W to 200 mW
To retain 75 hopping channels
  means overlapping FH channels
WBFH will be required to hop faster

## Slide 4: Potential uses of wider channels
Higher data rates are achievable
  higher signaling rates
  innovative modulation schemes increase rates even more
Better sensitivity for FSK due to possibility to use higher deviation
  today in 802.11 h=0.32
  optimum is at h=0.7
  gain of 4-5 dB in sensitivity and interference robustness
  beneficial to low power transmitters (WPAN)

## Slide 5: Will WBFH use more power than 802.11 systems?
The current regulations allow FH and DS 1 Watt
The proposed WBFH maximal power is 330 or 200 mW for 3 or 5 MHz wide channels, resp.
The part C of the response of 802.11 claims that
  802.11 devices typically use 100 mW
  WBFH devices will use full allowed power
This argument is an abuse
  the power used will be about same (at expense of range)
  depends on power consumption and amplifier cost

## Slide 6: Wideband FH interference is almost same as NBFH without power reduction
The NPRM intends to allow less power to WBFH than to NBFH.
In practice, the power will be similar
  maximum power is seldom used.
However, the interference to existing NBFH and DS users is not significantly different from the interference that this users cause to themselves and to each other!
Following slides address few scenarios.

## Slide 7: Analysis assumptions
The interferer transmitting from same distance at same power will be received at same total power
  spectral density will depend on bandwidth
The desired signal will be received at the power needed for demodulation
  approximately same spectral density
  WB signals need more received power, however it does not mean higher transmitted power, it means smaller useful range.

## Slide 8: WBFH interference to DS
The SINR depends (almost) only on FH signal power, not its bandwidth.
The DS-FH collision probability depends on DS BW and width of the hopping band, not on FH BW.
DS signal
NBFH
signal
WBFH
signal

## Slide 9: DS interference to NB and WB FH
WBFH needs more received power than NBFH, however SINR degradation due to DS jamer is same!
The DS-FH collision probability depends on DS BW and width of the hopping band, not on FH BW.
DS signal
NBFH
signal
WBFH
signal
SINR Degradation

## Slide 10: Interference of WBFH to NBFH
WBFH interferer needs more received power than NBFH, to fail a desired NBFH signal.
The collision probability for WBFH is higher, but the percentage of stations within range is smaller
NBFH signal
NBFH interferer
NBFH signal
WBFH interferer

## Slide 11: WBFH interference to itself - overlapping or disjoint channels?
Overlapping WBFH interferer creates slightly less interference
The collision probability for overlapping WBFH channels is twice as high.
Cochannel signals can use CCA to yield to others
  the CCA is not efficient with overlapping signals
WBFH signal
co-channel WBFH interferer
WBFH signal
overlapping WBFH interferer

## Slide 12: Summary
IEEE 802 should not issue a negative response to the FCC NPRM 99-149
  802.15 may benefit from it
  The interference to/from current systems is about same as among current incompatible systems
  IEEE should not block innovation
If IEEE decides to issue a negative response, it should remove the misleading assumptions about WBFH system transmit power compared to legacy systems.