## Slide 1
Update on RF Lighting Issue
Revised Proposal on In Band Emissions for RF Lights in 2.45 GHz ISM Band

## Slide 2
NPRM 98-42
Recommended authorization of RF Lights operating in 2.45 GHz ISM band
  NO LIMIT on in-band emissions!
  Only FDA limits on human exposure apply
  Final OET recommendation sent to Commission in December, 1998
Part 15 Interests appealed directly to Commission
  Commission delayed final resolution pending efforts of interested parties to seek resolution

## Slide 3
Unrestricted Devices
Can be used by public without special precaution
  e.g. microwave ovens
  Non-occupational limit is 1mW/cm2
  measured at 20 cm from any surface
By using point source approximation, de facto limit can be estimated:
  For r = 20 cm, surface of sphere:
    Area = 4  r2 = 5026 cm2
  EIRP of unrestricted device
    EIRP = 5026 cm2 x 1 mW/cm2 = 5 Watts!!!

## Slide 4
Restricted Devices
Can radiate at much higher power
  physical access must be barred
  same limit applies (1 mW/cm2)
  e.g. array of lights on a 12 meter mast
    applications include stadium lights, parking lots, etc.
    if tower is equipped with ladder, access is barred with a gate
    assume no one can come within 10 meters of lights
    Surface of sphere with 10 m radius is 12.5 x 106 cm2
  Allowable EIRP is 12.5 kW!!!

## Slide 5
Initial Proposal (Jan 99)

## Slide 6
Second Proposal (Mar 99)

## Slide 7
Latest Proposal (Jun 99)
2400
MHz
2500
MHz
2480
MHz
2460 - 2480 MHz
I
II
III
100 dBuV/m
@ 10 m
60 dBuV/m
@ 3 m
Region I
:
2400 - 2460 MHz. RF lighting restricted to 10 mV/m (avg)
Region II
:
2460 - 2480 MHz. RF Light emission limit of 100 dBuV/m @ 10 m
(equivalent to 330 mVm @ 3m). Consistent with CISPR15 limits.
Region III
:
2480 - 2500 MHz. RF lighting restricted to 10 mV/m (avg)
This portion of the band includes satellite services.
2460
MHz

## Slide 8
Magnetrons Sweep in Frequency

## Slide 9
Hi Ripple Power is Worst Case
Half Wave Rectified Power
Full Wave Rectified Power

## Slide 10
Effect of New Proposal
Requires RF Lights to use low (relatively) ripple DC power
  stabilizes magnetron operating frequency
  data from Fusion demonstrates that lights eqipeed in this manner can comply with new proposed limit
  operating BW of stabilized magnetron is <1 MHz
New limit restricts hi power to 2460 - 2480 MHz
  rest of band limited to 10 mV/m @ 3m (avg)
  Effective average power of -15 dBm