## Slide 1
Proposal for an improved B16 sequence
NTT
Masahiro Morikura and Masato Mizoguchi
morikura@ansl.ntt.co.jp

## Slide 2: A symbol timing detection scheme
Matched filter
Digital filter
Symbol timing decision
Received signals
Remove cyclic extension
Detected symbol timing
t9
t10
GI2
T1
t8
Matched filter output
Received training signal
Detecting disappearance of correlation peak signal

## Slide 3
Symbol Contents
Current short symbol pattern
Proposed B16 symbol(This modified B16 symbol pattern was accepted by the last ETSI BRAN meeting.)
Generated by 4 points cyclic time shift and rad rotation from current B16
Same PAPR and dynamic range with current B16


## Slide 4
Matched filter output
Matched filter output
B16
C64
B16
Time
Search was carried out to obtain low sidelobe at the neighborhood of mainlobe (around t=0) and the next short symbol period (t=16).

## Slide 5
Large correlation side-lobe degrades symbol timing detection accuracy
Matched filter output for direct path signal
Matched filter output
for delayed signal
t10
T1
t9
Disappearance of correlation peak signal
Influence of the high correlation side-lobe
on timing detection accuracy

## Slide 6
Packet error rate performance
Eb/N0 [dB]
Packet error rate
Packet error rate versus Eb/N0
The irreducible error caused by miss/false timing detection is much improved by using proposed B16 sequence.

## Slide 7
Conclusion
We propose to adopt the modified B16 short
symbol pattern which was accepted by the ETSI
BRAN.