## Slide 1: Enhancing 802.11 With QoS Introductory Discussion
Maarten Hoeben

## Slide 2: Why?
Why do we want to enhance 802.11?
  Technical reasons
    Integrate with modern LAN infrastructures
      802.1p
      IETF
    Enhance performance of 802.11
  Marketing
    HomeRF/Bluetooth
    Hype

## Slide 3: Why ? – NWN’s view
Enhancing performance.
Integration.
  IETF
Marketing.

## Slide 4: What Services?
Don’t drop straight into the fundamental discussions.

## Slide 5: What Services?
Ask the questions:
  What makes wireless different?
  What do we want to achieve?
  What is possible?
    What technology is available and feasible?
    What is feasible for a wireless LAN?
  Do we want to adapt the applications as well?
Result:
  Feasible services

## Slide 6: What Services ? - NWN’s view
What makes wireless different?
  Shared medium,
  Limited bandwidth,
  No guarantees,
  Mobility.
    Across cells

## Slide 7: What Services ? - NWN’s view
What do we want to achieve?
  We don’t want to achieve hard – real-time guarantees.
    Not feasible,
    Most applications don’t require them.
  Want to maintain wireless’ unique quality: mobility.
    Traditional bandwidth reservation may not be desirable.

## Slide 8: What Services ? - NWN’s view
What is possible?
  Soft real-time services
    Applications with playback points
      streaming video/audio
    Adaptive applications
    Bandwidth reservation
  Link parameters
    Packet delivery: bitrate, loss-rate (retry and fragmentation strategies).

## Slide 9: How ?
DCF
  Changing backoff mechanism.
    Simple to implement.
  Adding new contention mechanism.
    Requires major modification of the standard.
  Note that with both approaches it is difficult to integrate legacy devices.

## Slide 10: How ?
PCF
  Probably more complicated design, however:
    centralized scheduling makes it easier to meet certain service requirements,
    easy to integrate legacy devices, because they already adhere to PCF rules,
    more powerful platform.

## Slide 11: How ? - NWN’s view
Use PCF.
  Solve upstream scheduling problem.
    TxQueue state of station.
  Agree on a set of services and specify a mechanism for negotiating services.
  Find a balance between flexibility and complexity.
    Focus complexity in Access Point.