## Slide 1: Task Group d Report
September 13-17, 1999
Santa Rosa, CA

## Slide 2: Presentations
Extension of Frequency Hopping
  99/195, “Algorithmically Derived Hop Sequences”, Darwin Engwer, Johnny Zweig
    Tbaum@ee.rochester.edu (Edward Titlebaum)
Extension of Direct Sequence
  99/191, “Universal DS Channelization”, Bob O’Hara

## Slide 3: Discussion of International Mobility
Identified a set of parameters that can describe the channel allocation for FH, DS, HRDS, and OFDM PHYs.
  Created a new information element to carry the data
  Another element, or extensions to this element will be necessary for support of hop sequence distribution

## Slide 4: Channel Allocation Element
Regulatory identifier (2 octets)
Lifetime (1 octets)
Number of sub-elements (1 octet)
Each sub-element contains
  First channel center (2 octets)
  Channel spacing (1 octet)
  Number of channels (2 octets)
  Occupied bandwidth per channel (1 octet)
  Maximum transmitted power allowed (2 octets)

## Slide 5: Other Topics
Safe default operation until a channel allocation element is received (1 mW Tx power)
IBSS operation is in safe default mode until a channel allocation element is heard
  IBSS adopts channel allocation element heard from any(?) AP or other IBSS(?), lifetime is derivitive from original element
  Should IBSS allow user to set regulatory information?
What happens if conflicting information is received in different channel allocation elements?

## Slide 6: Worldwide 5GHz Requirements
Presented by Richard Paine, Boeing
WRC 2000 does not have 5GHz on the agenda
Opportunity to get 5GHz on the WRC 2002 agenda is during 6 weeks immediately after WRC 2000.
Request to have 802.11 send a letter to SG8 and/or WRC

## Slide 7: Motion
To have 802.11 send a letter to the US delegation of ITU SG8 and/or WRC suppporting the global allocation of the 5GHz band for unlicensed use.
  Passed unanimously