## Slide 1
NOKIA HARDWARE OVERVIEW
Olaf Joeressen
Nokia Mobile Phones
Olaf.Joeressen@nmp.nokia.com
Holger Hussmann
Nokia Mobile Phones
Holger.Hussmann@nmp.nokia.com
Thomas Müller
Nokia Mobile Phones
Thomas.T.Muller@nokia.com

## Slide 2: Outline
Properties Overview
Hardware
Architecture
Interfaces

## Slide 3: NOKIA Module: Facts
Flip-Chips: RF ASIC, BB ASIC, Flash
Size: < 500 mm2 (incl. Crystals)
Height: 2 mm
completely shielded
power supply: 3.0 .. 5.2 V
Interfacing: 1.8 .. 3.3 V

## Slide 4: NOKIA Architecture
Traditional high-IF RF
  fast time-to-market
  good sensitivity
SW oriented BB architecture
  only MIPS consuming tasks done in HW
    even low-level features can be added in SW
  No HW buffers dedicated to connections
    higher flexibility w.r.t. interfaces and buffer usage

## Slide 5: HW Blocks
Flash
RF ASIC
BB ASIC
- Rx/Tx
- regulators
- clocking
- Rx/Tx Control
- ARM7TDI
- CVSD codec
- Applic. IF
Control
Data
Bluetooth Module
Vappl
1.8V, 2.78
or 3.3V
Applic. IF
3.0 .. 5.2 V
13MHz
1.8 V
4
2
13 MHz
32 kHz

## Slide 6: NOKIA RF Part
SAW filter
Discriminator
tank
RF part
3.0 .. 5.2 V
Switch
2.4 GHz
RF ASIC
Rx:
- high IF limiting Rx
- analog FM discriminator
Tx:
- open loop Tx
- external VCO tank & varicap
- dig. pulse shaping
Internal regulators
Low pin-count RF/BB interface
13 MHz
VCO
Control
Data
13MHz
4
2
1.8 V

## Slide 7: NOKIA RF/BB Interface
Optimized for low pin count to aid integration of the BB functionality into existing system ASICs
  bi-directional data interface
  control bus can be shared with other ASICs
  timing control supported in the RF ASIC (e.g. synth. settling)

## Slide 8: NOKIA Baseband ASIC Facts
FlipChip package
ARM7 @ 13 MHz
32 kHz Sleep clock oscillator
Low-level (MIPS consuming) protocols in HW
Central buffer RAM (no dedicated buffers)

## Slide 9: Baseband ASIC - Block Diagram
Receiver
Clock,
Reset
Watchdog
Power
Control
Unit
HW Link
Controller
Buffer/MCU
RAM
MCU
Sybsystem
Data
Interface
Unit
ResetX
13 MHz
SysResetX
Clock
trunks

## Slide 10: More Common Bluetooth Interfaces needed ?
Drivers for common interfaces
  facilitate interoperability between components (HW/SW) from different vendors (Example: HCI)
Needed ?
  RF/BB: most important HW interface
    different vendors on both sides of Interface
    integrated BB solutions require stable interface
  HW/SW
    largely hidden in BB ASIC
    may depend on application

## Slide 11: Standard RF/BB Interface drivers
vendor-independent
RF-architecture independent
low-pin count
  enable BB integration into other ASICs
  reduce device pin count
future proofness
  Technology independent
  Higher data rates