## Slide 1
Multimedia Transport Over
Wireless LANs
Amar Ghori
Dr. Raju Gubbi
Sept 13, 1999

## Slide 2: Table of Contents
Introduction
Market Need
Tutorial on Multimedia Transmission
Characteristics
Requirements
Technical Feasibility

## Slide 3: Introduction - Goals for Presentation
Discuss the market dynamics for multimedia home networks
Introduce the technical issues surrounding transport of multimedia streams over wireless networks.
Encourage the creation of a PAR

## Slide 4: Market Needs
Key benefits
Market drivers
Analyst View
Consumer Interest

## Slide 5: Consumer Benefits of Multimedia Networks
Lets Users Consume Content in Preferred Locations
  Allows access from any room
  Provides for both stationary and mobile appliances
Reduces the Cost of Appliances
  Leverages compute power & peripherals of “media server”
  Central upgrade point mitigates obsolescence
Enables “Sharing” Among Appliances
  Content sharing
  Peripheral sharing
  Connection sharing
Content Use Is More Enjoyable, Convenient and Affordable

## Slide 6: Home Multimedia Drivers/Trends
  Broadband is a Key Driver for Multimedia Content
    45 million homes with broadband (cable & dsl)access by 2002
    Multimedia apps key driver of broadband demand
      63% cited downloads of audio, video & games files
      54% would increase consumption of streaming
  Streaming Media Trends
    65 million downloads of RealPlayer
    2000 radio and TV stations broadcasting on the internet
    Many major service providers looking at remote applications
  Stored Media Trends
    14 million DVRs (e.g., TiVO, Replay) by 2004
    Digital audio now a industry phenomena
      180 million MP3 files downloaded on a weekly basis
      30M portable MP3 players (e.g., Rio) by 2003
      MP3 will be > $1 billion business by 2003
    Digital cameras & v-conferencing > $1 billion by 2003

## Slide 7: Market Evolution of Multimedia Network Devices
Broadband Modems
Residential
Gateways
Set-Top
Boxes
Broadband Modems
PCs (Desktop & Notebook)
TVs (Analog & Digital)
Mobile Pads
Kitchen Pads
Enhanced PDAs
Cordless Phones
DVD Players
Cable/DBS Boxes
Videoconferencing Cameras
Hosts
Nodes
TV Terminals
Mobile Pads
Desktop PCs
1999
2000
2001+
Desktop PCs
PDAs
Notebook PCs
Notebook PCs
Desktop PCs
Desktop PCs
Desktop PCs
Broadband Modems
Residential
Gateways
VoIP
Phones

## Slide 8: Multimedia Network Adoption
Source: Parks Associates Connections’99 Workshop.
Millions of Dollars
Home Entertainment Networks (non-PC) Projections based on
Average Penetration of CE products
Entertainment networks Penetration rate
Nodes per household

## Slide 9: Consumer Interest in Multimedia Networking
0
10
20
30
40
50
60
70
80
90
Data only LAN
MM LAN
Interest in Home Multimedia LAN
Performance
Ease Of Use
Media
Quality
Desired Attributes
* 279 US Households Survey

## Slide 10
Tutorial: Transporting Multimedia Over 802.11b Wireless LANs
Dr. Rajugopal Gubbi
Sept 13, 1999

## Slide 11: Asynchronous data v/s multimedia (MM) Streams
Asynchronous Data
Little or no latency restrictions
Real-time delivery not an issue
All data frames are treated equally
Multimedia streams
Need security due to copyright restrictions
Sensitive to latency in delivery
Network throughput is an issue as it controls how many MM streams can be efficiently supported at a given time
All MM frames can NOT be treated equally
Hence need stream support at the MAC level
Further needs dynamic management of the network resources

## Slide 12: What is a stream?
A stream is a set of frames requiring specific services and a specific range of parameter values for the required services. Some of the examples of the services are;
  Latency: How often the stream frames are transmitted independent of the network traffic conditions.
  Bandwidth: How many stream frames are transmitted per second independent of the network traffic conditions.
  Priority: How important is this stream compared to other traffic on the network
  Channel protection: How much error correction or retransmission is carried out on the frames of the stream.
Streams are virtual connections over the basic MAC/PHY services of transmission and reception of frames.

## Slide 13: What is needed for Multimedia data transport (1)?
The requirements of transporting multimedia streams over LANs are grouped into three broad categories. They are; Latency, Bandwidth Management, and Channel Throughput
Latency
  Streams from interactive applications demand tighter latency in delivery. While voice streams require the latency to be less than 10ms, a video stream can tolerate latencies up to 100ms (or about 3 frames).
  For streams from non-interactive real-time applications, latency jitter increases the buffer size required at the receivers.
  Hence the LAN should support a stream to be transmitted at pre-negotiated intervals of time.

## Slide 14: What is needed for Multimedia data transport (2)?
Bandwidth Management
  MM stream support needs a mechanism for an STA to negotiate and obtain the required bandwidth
  Since the start and end of a stream or the content of the stream is unpredictable at the MAC level, there is a need for a simple mechanism to negotiate/re-negotiate the bandwidth required by each STA.
  Since different MM streams could have different priorities, priority management is needed to transport the most important streams with appropriate quality (guaranteed service)
  Due to the limited number of PHY channels, efficient bandwidth management across coordinators is essential.

## Slide 15: What is needed for Multimedia data transport (3)?
Channel Throughput
  Collision free operation increases the channel throughput and reduces latency of delivery
  Without error detection/correction, one bit error could mean
    for voice stream, loss of up to 10ms worth of data
    for video stream, in the worst case scenario, corrupted data frame could mean the entire video frame or even all the remaining picture frames in the current group of frames being dumped
  Channel errors reduce the channel throughput with no error correction
    25% PER is typical in the home environment
  With error correction, the channel throughput required for the multimedia streams can be sustained
  Extreme interference in the channel means finding a better channel to support the throughput required by the multimedia streams

## Slide 16
Isochronous support over lossy medium is a difficult task. However, simple-but-clever multimedia coordination can achieve the same goals
MM stream support does not necessarily need different mechanisms for authentication/ de-authentication / association/ re-association/ disassociation
Improved ease-of-use desirable for installation, authentication, security and channel selection
Encryption is required in order to preserve the copyright restrictions on multimedia data along with the privacy of the user
Backward compatibility should not be ignored
What else is needed or not needed?

## Slide 17: Is a solution possible?
A solution should be possible that…
    Meets the market’s needs
    Requires no changes to current STA
    Enhances 802.11 to encompass applications beyond data
    Is technically feasible and low cost