## Slide 1: IEEE 802.11 Overview and Completed Amendments Overview of the 802.11 Working Group The IEEE 802.11 standard to date Completed Amendments: Markets, use cases and key technologies 2025 January Presenter: “At lectures, symposia, seminars, or educational courses, an individual presenting information on IEEE standards shall make it clear that his or her views should be considered the personal views of that individual rather than the formal position, explanation, or interpretation of the IEEE.” IEEE-SA Standards Board Operation Manual (subclause 5.9.3)

## Slide 2: IEEE Standards Association
6,879 individual members in 90 countries
Individual membership
  187 member corporations in 23 countries
Corporate Memberships
  ~20,000 participants;
  all interested parties are welcome
Standards Developers
Maintaining the Standard
Initiating the Project
Mobilizing the Working Group
Drafting the Standard
Balloting the Standard
Gaining Final Approval

## Slide 3: The IEEE 802.11 Working Group is one of the most active WGs in 802
802.3
CSMA/CD
Ethernet
802.24
Vertical
App. TAG
802.11
Wireless
WLAN
802.15
Wireless
Specialty
Networks
802.21
Media
Independent
Handoff
802.19
Co-existence
WG
IEEE 802
Local and Metropolitan Area Networks
Standards Committee (LMSC)
802.18
Radio
Regulatory
TAG
802.16
Wireless
Broadband
Access
802.22
Wireless
Regional
Area
Networks
802.1
Higher
Layer
LAN
Protocols
IEEE 802.11 WG Voting Members: 300+
OSI Reference
Model
Application
Presentation
Session
Transport
Network
Data Link
Physical
Medium
IEEE
802
Focus on link and physical layers of the network stack
Leverage IETF protocols for upper layers

## Slide 4: Type of Groups in 802.11
Type of Group | Description
WG | Working Group
SC | Standing Committee
TG | Task Group
SG | Study Group
TIG | Topic Interest Group
AHG | Ad Hoc Group
January 2025
4

## Slide 5: Development of the IEEE 802.11 Standard is ongoing since 1997
802.11-2024
802.11-2003
MAC
PHY & MAC
11d
Intl Roaming
11b
HR/DSSS
11 Mb/s in 2.4 GHz
11a
OFDM
54 Mb/s in 5 GHz
802.11-1997
802.11-2007
11e
QoS
11h
DFS & TPC
11i
Security
11f
Inter AP
11j
JP bands
11g
54 Mb/s in 2.4 GHz
802.11-2012
11k
RRM
11s
Mesh
11u
WIEN
11v
WNM
11z
TDLS
11r
Fast Roam
11w
Management Frame Security
11n
High Throughput (>100 Mb/s)
11p
WAVE
11y
Contention Based Protocol
802.11-2016
11af
TV Whitespace
11ac
VHT
> 1 Gb/s in 5 GHz
11ad
VHT
> 1 Gb/s in 60 GHz
11ae
QoS Mgt Frames
11aa
Video Transport
802.11-2020
11ah
Sub-1 GHz
11aj
China mmWave
11ai
Fast Initial Link Setup
11ak
General Link
11aq
Pre-association Discovery
11bc
Broadcast Services
11bb
Light Communications
11az
Enhanced Positioning
11ba
Wake-up Radio
11ax
High Efficiency WLAN
11ay
Enhanced mmWave
11bd
Next Gen V2X
802.11-1999
Notes: doc.: IEEE 802.11-11/0483r0
May 2011
        Bruce Kraemer (Marvell)
Page 5
The 802.11 Working Group was established in 1990. The first standard was published in 1997 (2.4GHz) supporting 1 and 2 Mbps. Subsequent amendments and revisions have increased radio performance and throughput by orders of magnitude.
The 802.11b 11Mbps standard was the first to achieve commercial success, with the announcement by Steve Jobs at MACWorld in 2001 that the MACbook would include 802.11 radios, along with the Apple Airport. PC vendors followed suit. Describe highlights of each revision.

## Slide 6: Completed 802.11 technologies to meet expanding market needs and leverage new technologies - 1
802.11ah – Operating in license-exempt bands below 1 GHz (excl. TV bands)
802.11ai – Fast initial link set-up
802.11aj – Enable 802.11ad operation in the Chinese 59-64 GHz frequency band.
802.11ak – General Link
802.11aq – Pre-association Service Discovery
802.11ax – Increased throughput in 2.4, 5 (and 6) GHz bands. Increased efficiency.
802.11ay – Support for 20 Gbps in 60 GHz band.
ARC – Architecture (Ongoing discussion topics)
Notes: Here is a list of completed amendments. ARC is an ongoing IEEE 802.11 architecture discussion group

## Slide 7: Completed 802.11 technologies to meet expanding market needs and leverage new technologies - 2
802.11az – 2nd generation positioning features.
802.11ba – Wake up radio. Low power IoT applications.
802.11bb – Light Communications
802.11bc – Enhanced Broadcast Service
802.11bd – Enhancements for Next Generation V2X
802.11be – Extremely High Throughput in 2.4, 5 and 6 GHz bands
Notes: Here is a list of amendments currently under development.

## Slide 8: 802.11ah defines OFDM PHY and MAC operating in license-exempt bands below 1 GHz (excl. TV bands)
Define OFDM PHY and MAC operating in license-exempt bands below 1 GHz (excl. TV bands)
  Extended range
  Power efficiency
  Large number of devices
Potential Applications
  Internet of everything (IoT)
  Smart Grid
  Healthcare
  Smart Appliances
  Wearable consumer electronics
Monitor
January 2025
8

## Slide 9
PHY
OFDM (FFT size 32 and 64)
New reliable MCS-10 working with larger delay spread and Doppler for outdoor
Diverse data rates:150Kbps-347Mbps
Range >1 km
MAC
Scalability up to 8191 devices per AP
    Restrict Access Window operation
    Hierarchical TIM structure
Efficient frames and transmissions
    Short frame format
    Short control/mgmt. frames
    Asymmetric & bi-directional transmissions
Reducing power consumption
    Non-TIM operation
    Target Wake Time mechanism
    Extended sleeping and listen interval
Relay Operation
20 MHz
16
8
4
2
1
150 Kbps – 4 Mbps
5.8-78 Mbps*
Mandatory & Globally Interoperable modes optimized for sensor networking
Optional higher data rate modes for extended range -
Minimum 11n/ac bandwidth
11ah bandwidths
*For 1 spatial stream and normal guard interval only. 11ah supports up to 4 spatial streams and short guard interval providing data rates up to ~347 Mbps
802.11ah technical features
January 2025
9

## Slide 10: 802.11ai defines fast initial link set-up methods
This amendment defines mechanisms that provide IEEE 802.11 networks with fast initial link set-up methods which do not degrade the security currently offered by Robust Security Network Association (RSNA) already defined in IEEE 802.11.
The project’s primary need came from an environment where mobile users are constantly entering and leaving the coverage area of an existing extended service set (ESS).
  scale with a high number of users simultaneously entering an ESS
  minimize the time spent within the initial link set-up phase
  securely provide initial authentication.
January 2025
10

## Slide 11: 802.11ai technical features
802.11ai reduces connection setup overhead by:
AP
STA
DHCP
Beacon/Probe Resp
Auth Req/Resp
AS
Association & IP addr
AP
STA
DHCP
Authentication
Association
EAPOL Key
DHCP
AS
EAP
(PEAP/MSCHAPv2)
11i
11ai
Improvement on scanning
  More control on scanning procedures or association attempt
  Neighbor BSS or channel information in Beacon, Probe Response and FILS Discovery frame
FILS Authentication protocol
  FILS shared key authentication with or without PFS
  Public key authentication method with PFS
Higher Layer Setup during Association/Reassociation
  Higher Layer Protocol encapsulation
  FILS IP configuration
January 2025

## Slide 12: 802.11aj defines modifications to 802.11ad to enable operation in the Chinese 59-64 GHz frequency band
This amendment defines modifications to the IEEE P802.11ad Physical (PHY) layer and the Medium Access Control (MAC) layer to enable operation in the Chinese 59-64 GHz frequency band.
The amendment maintains backward compatibility with 802.11ad when it operates in the 59-64 GHz frequency band.
The amendment also defines modifications to the PHY and MAC layers to enable the operation in the Chinese 45 GHz frequency band. The amendment maintains the 802.11 user experience.
January 2025
12

## Slide 13: 802.11aj technical features
11aj considers the following:
Link Budget Analysis for 40-50 GHz Indoor Usage
Multi-Carrier Training Field for OFDM Transmission in the 45GHz
Packet Encoding Solution for 45GHz
A Proposed frame structure is as follows
January 2025

## Slide 14: 802.11ak enables an 802.11 connection to be used as a through link in a general network
This amendment enables an 802.11 connection to be used as a through link in a general network, not just as a connection to an end station at the edge of a network.
Fully general mixed 802.11 and wired plug and play in the home.
Data Center top-of-rack to top-of-rack connections for overflow traffic.
Industrial and Enterprise network use.
January 2025
14

## Slide 15: 802.11aq enables the delivery of pre-association Service Discovery information
A typical use case is printer discovery in a hotel
Pre-association protocol designed to discover services on a WLAN
January 2025
15

## Slide 16: 802.11aq technical features
Container MAC protocol to carry upper layer service discovery protocols (e.g. UPnP, Bonjour)
Provisioning and configuration of services in the access point
  Service Transaction Proxy is a logical element connected to the access point
Universal identification of services
  Using a hash name
  Provide service attributes (e.g. 3D printer capability or point of sale service)
Currently considering request/response or broadcast concept
16
January 2025

## Slide 17: 802.11ax is focused on improving performance in dense environments
Existing 802.11 WLAN systems serve dense deployments: 2019 Super bowl: 24TB* of data carried on WLAN network
802.11ax aims to further improve performance of WLAN deployments in dense scenarios
  Targeting at least 4x improvement in the per-STA throughput compared to 802.11n and 802.11ac.
  Improved efficiency through spatial (MU MIMO) and frequency (OFDMA) multiplexing.
Dense scenarios are characterized by large number of access points and large number of associated STAs deployed in geographical limited region
  e.g. a stadium or an airport.
  * https://www.extremenetworks.com/resources/slideshare/wi-fi-engagements-from-super-bowl-liii/
Access to Internet, latest airlines’ announcements, and digital media such as movies and sport events
17
January 2025
Notes: Reference: https://www.extremenetworks.com/resources/slideshare/wi-fi-engagements-from-super-bowl-liii/
AX is the next major MAC PHY that will come to the market. Already some products R&D announced. More be shipped and certified in 2019
Primary goal of 802.11 AX is to improve the performance of wireless LANs in dense scenarios. Targeting at least 4x improvements in the throughput per client device over 802.11n and ac.
Technologies used are MU-MIMO and OFDMA

## Slide 18: 802.11ax Categories of Enhancements
Outdoor / Longer range
Power Saving
High Density
Spectral Efficiency & Area Throughput
8x8 AP
1024 QAM
25% increase
in data rate
OFDMA
Enhanced delay
spread protection-
long guard interval
Scheduled sleep and wake times
20 MHz-only clients
Spatial Reuse
DL/UL MU-MIMO
w/ 8 clients
0.8us 11ac
1.6us 11ax
Extended range packet structure
3.2us 11ax
2x increase
in throughput
ac
ax
Up to 20%
increase
in data rate
Long OFDM
Symbol
18
January 2025

## Slide 19: OFDMA enables further AP customization of channel use to match client and traffic demands
Increased efficiency for (high percentage of traffic) short data frames
19
Notes: OFDMA is a radio modulation technique that provides the ability to customize at very low level the channel use to match client and traffic demands.
You can see the pictorial difference between OFDM and OFDMA.
- In OFDMA, it is possible to provide service to multiple users during the same time and frequency, especially when there are high % of traffic consists of short data frames. This provides extreme improvement in the efficiency.
OFDMA allocates subsets of frequency to specific users. OFDMA enables greater flexibility to send data to multiple users at the same time.
This technique can reduce delay and latency for traffic.

## Slide 20: BSS Coloring enables additional channel re-use
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
All same-channel BSS block
Same-channel BSS only block on Color Match
20

## Slide 21: 802.11ax Increases link efficiency
Squeeze more tones in around DC and edge
Frequency domain
(~5% gain)
DATA
GI
DATA
GI
…
DATA
GI
DATA
GI
DATA
GI
DATA
GI
DATA
GI
…
4 times
FFT window
Time domain
(~15% gain)
Guard interval (GI) overhead reduced
Modulation
(~25% gain)
+ 1024-QAM
Increased tone density
VHT
HE
VHT
HE
21
January 2025
Notes: This slide shows the techniques that are used in 802.11 ax to obtain the improvements in link efficiency. They can applied in 3 domains: Frequency domain, Time domain, and Modulation.

## Slide 22: UL/DL multi-user links in 802.11ax will support more efficient UL data
  In a VHT UL sequence, STAs compete for medium access and send sequentially
  In an HE UL sequence, the AP triggers simultaneous transmissions in multiple STAs
VHT
HE
UL Data (STA 1)
DL BA (STA 1)
UL Data (STA 2)
DL BA (STA 2)
UL Data (STA n)
DL BA (STA n)
Trigger
Preamble
UL Data (STA 1)
:
Data (STA n)
Multi-STA BA
(STA 1-n)
22
January 2025

## Slide 23: 802.11ax Data exchange sequences: Multi-user downlink
In a VHT DL MU sequence acknowledgements are serialized
In an HE DL MU sequence acknowledgements are allocated UL resources and transmitted simultaneously
BA STA #n
: :
BA STA #2
BA STA #1
Preamble
DL Data (STA 1)
:
DL Data (STA 4)
BAR
BA STA #1
BA STA #2
BAR
BA STA #4
Preamble
DL Data (STA 1)
:
DL Data (STA 4)
VHT
HE
23
January 2025

## Slide 24: Uplink MU-MIMO
UL MU-MIMO was initially considered in 802.11ac, but not included due to implementation concerns
Sounding frames, data frames, etc can be grouped among multiple users to reduce overhead and increase uplink response time
8x 1SS
24

## Slide 25: Various features in 802.11ax will support improved outdoor operation
  Operates in higher delay spread channels than 802.11ac:
    802.11ac GI options: 0.4 µs and 0.8 µs
    802.11ax GI options: 0.8 µs, 1.6 µs and 3.2 µs
    GI overhead mitigated with longer OFDM symbol
  Preamble includes repeated L-SIG
  Extended range preamble includes repeated HE-SIG-A
  Dual carrier modulation improves robustness in Data field
25
January 2025

## Slide 26: 802.11ax meets the MAC/PHY requirements for 5G Indoor Hotspot test Environment defined by IMT-2020
Analysis and simulations confirm that performance of IEEE 802.11ax MAC/PHY meet or exceed 5G requirements for the 5G Indoor Hotspot use case
Similar studies are underway for the Dense Urban test environment
 | Metric | ITU-R Evaluation Method | Minimum Requirement | 802.11ax Performance
1 | Peak data rate | Analytical | DL/UL : 20/10 Gbps | DL/UL : 20.78 Gbps [Note 1]
2 | Peak spectral efficiency | Analytical | DL/UL : 30/15 bits/s/Hz | DL/UL : 58.01 bits/s/Hz [Note 2]
3 | User experienced data rate | Analytical for single band and single layer; Simulation for multi-layer | Not applicable for Indoor Hotspot | Not applicable
4 | 5th percentile user spectral efficiency | Simulation | DL/UL : 0.3/0.21 bits/s/Hz | DL/UL : 0.45/0.52 bits/s/Hz [Note 3]
5 | Average spectral efficiency | Simulation | DL/UL : 9/6.75 bits/s/Hz/TRxP | DL/UL : 9.82/13.7 bits/s/Hz/TRxP [Note 3]
6 | Area traffic capacity | Analytical | DL : 10 Mbit/s/m2 | Required DL bandwidth = 170 MHz with 3 TRxP/site. [Note 4]
7 | Mobility | Simulation | UL : 1.5 bits/s/Hz | UL : 9.4 bits/s/Hz
8 | Bandwidth | Inspection | 100 MHz, scalable | 20/40/80/80+80/160 MHz
9 | User plane latency | Analytical | DL/UL : 4 ms | DL/UL : 80 us [Note 5]
26

## Slide 27: 802.11ay is defining next generation 60 GHz: increased throughput and range
Use Cases:
  Ultra-Short Range
  8K UHD - Smart Home
  AR/VR and wearables
  Data Center Inter Rack connectivity
  Video / Mass-Data distribution
  Mobile Offloading and MBO
  Mobile Fronthauling
  Wireless Backhauling (w. multi-hop)
  Office Docking
  Fixed Wireless
Key additions :
  SU/ MU MIMO, up to 8 spatial streams
  Channel bonding
  Channel aggregation
  Non-uniform constellation modulation
  Advanced power saving features
20Gbps+ rates are defined
License- Exempt bands above 45Gbps
Completion in 2020; First chipsets announced
27
January 2025

## Slide 28: 60 GHz Fixed Wireless Use Case: Affordable 5G Performance
https://www.fiercewireless.com/wireless/60-ghz-band-particularly-appealing-for-fixed-wireless-report
“the 14 GHz of contiguous spectrum in the band offers more bandwidth than any other licensed or unlicensed mmWave band. Further, the 60 GHz band has chipsets and technology currently available on the commercial market.”
“In the U.S., unlicensed mmWave frequencies available for 5G primarily cover the band from 57 – 71 GHz, called the V-Band, or 60 GHz band. This band offers 14 GHz of contiguous spectrum, which is more than all other licensed and unlicensed bands combined7. This makes the 60 GHz band an excellent alternative to licensed mmWave frequencies for smaller providers, as it can be used to deliver 5G performance for the minimal cost of available 60 GHz infrastructure products.
https://go.siklu.com/hubfs/Content/White%20Papers/Maravedis%20Industry%20Overview:%205G%20Fixed%20Wireless%20Gigabit%20Services%20Today.pdf
28
January 2025

## Slide 29: 60 GHz Mesh Backhaul Wireless Use Case: Deploying Today
“Leading Wi-Fi and wireless network solution vendor Cambium Networks announced today that they will be incorporating Facebook’s Terragraph technology into a new series of Cambium Networks 60 GHz radio products called cnWave™. The news comes as Terragraph appears to be ramping up go-to-market activities with trials underway in Hungary and most recently in Malaysia.”
“Terragraph is essentially a 60 GHz-based meshed (or multi-hop, multi-point) backhaul radio system for deployment at street level in cities.”
https://wifinowevents.com/news-and-blog/cambium-networks-to-incorporate-facebook-terragraph-tech-into-new-60-ghz-products/
29
January 2025

## Slide 30: 802.11ay builds on 802.11ad with MIMO and channel bonding features
Channel bonding and aggregation requires new:
  Channelization
  Packet format
  Channel access mechanisms
Single User and downlink MU MIMO
  Distribute capacity across users
  Unique requirements given directionality
  Exploit antenna polarization
  Changes to the beamforming protocol
Example without polarization
Example with polarization
30
January 2025

## Slide 31
802.11ay defined channelization
31
January 2025

## Slide 32: 802.11az Next Generation Positioning
The P802.11az project Next Generation Positioning extends accurate IEEE Std 802.11-2016 Fine Timing Measurement capabilities
Accurate indoor Navigation (sub 1m and into the <0.1m domain).
Enables self-locating networks for easy, fast and cost efficient WLAN deployment for navigation and 6GHz AFC operation.
Secured (authenticated and private) positioning – open my car with my smartphone, position aware services (money withdrawal).
Unlock computer with a wearable device, adapt TV content to audience presence.
Location based link adaptation for home usages (connect to best AP).
Navigate in extremely dense environments (stadium/airport scenarios).
32
January 2025

## Slide 33: 802.11az Key Radio and Positioning Techniques
Medium efficient operation via dynamic (demand dependent) measurement rate
Adaptation to next generation mainstream 802.11ax Trigger Based Operation (MIMO, Trigger Frame, NDP frame)
Authenticity and privacy and anti-spoofing mechanism via PMF in the unassociated mode and PHY level randomized measurement sequences (HE LTF sequences protection)
Improved accuracy via MIMO and larger BW available in the <7Ghz band for 11ax
MIMO enablement for measurement for improved accuracy especially for NLOS or NNLOS conditions
Passive location with fixed overhead independent of number of users
January 2025

## Slide 34: 802.11ba Wake-up Radio Main Use Cases
1. Smart Home
2. Warehouse
3. Wearables
WUP: wake-up packet
WUR: wake-up receiver
MR: main radio
34

## Slide 35: 802.11ba improves energy efficiency of stations and maintains low latency
802.11 radio needs to wake up periodically to receive data within a latency requirement  high power consumption of 802.11 station
Internet
AP buffers data until the 802.11 station wakes up
 Long latency
802.11 station
Awake
Sleep
Short sleep interval
Do you have data for me?
No
Buffer
Internet
802.11 station
Awake
Sleep
Long sleep interval
Buffer
data
data
Do you have data for me?
Do you have data for me?
No
No
35
January 2025
January 2025
Notes: 802.11ba focuses on improving the power efficiency of 802.11 stations, enabling longer batter life.

## Slide 36: 802.11ba Low-power Wake-up Receiver (LP-WUR) as Companion Radio for 802.11
Comm. Subsystem = Main radio (802.11) + LP-WUR
  Main radio (802.11): for user data transmission and reception
    Main radio is off unless there is something to transmit
    LP-WUR wakes up the main radio when there is a packet to receive
    User data is transmitted and received by the main radio
  LP-WUR: not for user data; serves as a simple “wake-up” receiver for the main radio
    LP-WUR is a simple receiver (doesn’t have a transmitter)
    Active while the main radio is off
    Target power consumption < 1 mW in the active state
      Simple modulation scheme such as On-Off-Keying (OOK)
      Narrow bandwidth (e.g. < 5 MHz)
    Target transmission range: LP-WUR = Today’s 802.11
36
January 2025
Notes: 802.11ba introduces the use a a “wake-up receiver” which can remain active at extremely low power, detecting when traffic is present for the main radio.

## Slide 37: 802.11ba Low Power Wake-up Radio Operation
802.11
802.11
802.11
802.11
LP-WUR
ON
Wake-up Packet
Data
Packet
Wake-up signal
Transmitter
+
Receiver
Transmission range
802.11 = LP-WUR
ON
OFF
ON
OFF
Wake-up Packet
or
802.11
37
January 2025

## Slide 38: 802.11bb Light Communications
Use Cases:
  Industrial wireless applications
  Medical environments
  Enterprise
  Home
  Backhaul
  Vehicle to Vehicle Communication
  Underwater Communication
  Gas Pipeline Communication
Key additions :
  Uplink and downlink operations in 800 nm to 1000 nm band
  Minimum single-link throughput of 10 Mb/s
  Interoperability among solid state light sources with different modulation bandwidths.
Light Communications (LC)
  Ability to re-use existing HT, VHT and HE PHY/MAC
38
January 2025

## Slide 39: 802.11bb transports defined 5/6GHz MAC/PHY across the light channel
5/6 GHx 802.11 MAC and PHY are used as defined today
A Physical Layer Protocol Data Unit (PPDU) is converted to light using intensity modulation. At the receiver, the optical signal is converted to an electrical signal. LC systems transmit on wavelengths within the 800nm to 1000 nm band.
802.11
MAC
Existing
PHY for LC
LC
TX/RX
802.11
MAC
LC
TX/RX
Existing
PHY for LC
January 2025

## Slide 40: 802.11bb uses light spectrum and existing WLAN capabilities
RF frontend up-converts baseband signals onto e.g. fc= 5 GHz.
LC frontend up-converts baseband onto low IF e.g. fc= BW/2 + Δ.
  Δ is specified in the existing draft of TGbb for various channel bandwidths.
In this manner, LC re-uses the existing HT, VHT and HE PHY/MAC specifications.
5 GHz
BW/2 + Δ MHz
January 2025

## Slide 41: 802.11bb uses light spectrum and existing 802.11 technical capabilities
Example implementation of P802.11bb using up- and down-conversion of existing 5 GHz or 6 GHz chipsets
Interfacing the LC PHY to light emitter and receiver.
January 2025

## Slide 42: 802.11bb usage model 1: Industrial wireless
Pre-Conditions
Devices may experience unstable radio frequency (RF) connection due to Electro-Magnetic Interference (EMI) in factories. LC is deployed to provide reliable wireless connectivity for industrial wireless networks.
Environment
All communications are within a large metal building, industrial or automated work cell. The area of these environments range from tens to thousands of square meters, equipped with industrial robot and other equipment. The environment has high levels of EMI. Lighting level of 150 lux is recommended (1500 lux for dedicated work).
Applications
Ultra-high-definition (UHD) video streaming for surveillance or production monitoring (quality control) applications, for video collaboration for team, customer, and supplier meetings. Lightly compressed Video: ~ 1Gbps, delay < 5 ms, 1x10-8 PER, 99.9% reliability. Fully connected factory—for real-time communications, application execution, and remote access.Distance between LC APs ranges from 2~20 meters.
Traffic Conditions
Both uplink and downlink traffic is using LC.
High levels of OBSS interference between LC access points (APs) expected due to very high density deployment.
Potential non-LC interference from surrounding environments such as artificial-light.
Multiple LC modules are deployed on the robot/equipment and on the ceiling/walls to provide multiple light links for a robust connectivity in case a single line-of-sight (LOS) link is blocked.
Use Case
An industrial robot is powered on and ready for operation.
Operating instructions are transmitted to the robot via LC.
The robot is working (e.g., movement) according to the instructions and provides real-time feedback information and/or video monitoring data for quality control to control center also via LC. Upon command, the robot finishes the task and is ready for the next one.
January 2025

## Slide 43: 802.11bb usage model 2: Wireless access in medical environments
Pre-Conditions
IEC 60601-1-2 standard recommends the minimum separation distance between medical electrical (ME) equipment and RF wireless communications equipment (e.g., wireless local area network (WLAN)) be 30 cm to avoid performance degradation of the ME equipment. LC is deployed to ensure the performance of all ME equipment.
Environment
The size of a operating theater and MRI room ranges from 30~60 m2. Multiple LC-APs are deployed on the ceiling to provide specialized illumination. The central illuminance of the operating light: 160k and 40k lux. The size of a four beds ward is about 60 m2, light level: 300 lux on the bed and >100 lux between the beds and in the central area.
Applications
LC-WLAN is used to allow wireless data exchange in medical environments with ME equipment or system.
Medical multimedia and diagnostic information can be transmitted to provide telemedicine services; ME equipment can also be wirelessly controlled via LC.
Provide Intranet/ Internet access, audio or video call for doctors, nurses and patients using LC-based devices.
Traffic Conditions
No interference caused by RF radiation.
Both uplink and downlink traffic is are using LC.
High Quality of Service (QoS) and high reliability are required.
Potential non-LC interference from surrounding environments such as artificial-light.
Use Case
Doctors enter an operating theater, turn on the LC enabled LED lights and ME equipment. Doctors can interact with the remote doctors and share information using LC. ME equipment connectivity is also supported by LC. Doctors finish the treatment, then turn off the lights and medical equipment.
A patient is monitored by ME equipment which communicate with the nurses/doctors in control room via LC.
© vm
Operating theater
Hospital ward
January 2025

## Slide 44: 802.11bc is defining Enhanced Broadcast Services
Enhanced Broadcast Services (eBCS) defines broadcast service enhancements within an 802.11-based network.
Client end devices broadcast information to an AP, e.g. in an IoT environment, to other STAs so that any of the receiving APs act as an access node to the Internet.
January 2025

## Slide 45: 802.11bc Broadcast Downlink use case description
Broadcast Downlink
  Provides enhanced Broadcast Services (eBCS) of data (e.g. videos) to a large number of densely located STAs.
  These STAs may be associated, or un-associated with the AP or may be low-cost STAs that are receive only.
Topology/Architecture
Contents
Server
AP
STA
STA
STA
STA
Network
STA
January 2025

## Slide 46: 802.11bc Broadcast Uplink use case description
Broadcast Uplink
  Pre-configured devices (e.g. IoT) automatically connect to the end server through APs with zero setup action required.
  Alternatively, low power IoT devices that are in motion, report to their servers through APs without scanning and associating
Internet
Server
STA 1
STA 2
Topology/Architecture
Internet
Server
AP 1
STA 1
@ t=T1
AP 2
STA 1
@ t=T2
Zero Setup Sensor
Sensor on the move
AP 1
AP 2
January 2025

## Slide 47: 802.11bd defines an evolution of 802.11p for Vehicle to Anything (V2X)
802.11p is largely based on 802.11a.
802.11bd defines MAC/PHY enhancements from 802.11n, ac, ax, to provide a backwards compatible next generation V2X protocol.
Higher Throughput
  OFDM frame design
  Higher MCS, LDPC coding
  Packet aggregation
Longer Range
  Mid-amble design
  Repeated transmission mechanism
  More robust channel coding
Support for Positioning
Backward Compatibility
  Backward compatible frame format design, Version indication
Longer Range
Higher Throughput
Backwards Compatibility
Positioning
January 2025

## Slide 48: 802.11bd: Next Generation V2X Use Cases
V2X Use Cases:
  Suport all defined DSRC/802.11p use cases, including Basic safety message (safety, range, backward compatibility, fairness)
  Sensor sharing (throughput)
  Multi-channel operation (safety channel + other channels)
  Infrastructure applications (throughput)
  Vehicular positioning & location (LoS and NLoS positioning accuracy)
  Automated driving assistance (safety, throughput)
  Aerial vehicle IT application (video)
  Train to train (high speed)
  Vehicle to train (high speed, long range)
Key additions :
  Higher throughput (2x) than 802.11p
  Longer range (3dB lower sensitivity level)
  Support for positioning
  Backward compatibility with 11p
5.9 GHz band mainly, and optionally 60 GHz;
Completion in 2022/2023
http://www.ieee802.org/11/Reports/tgbd_update.htm
48
January 2025

## Slide 49: 802.11be Extremely High Throughput amendment builds on 802.11ax, including 6GHz support
Use Cases:
  Home, enterprise, industrial, IoT
  Outdoor
  AR/VR, wireless gaming
  4K and 8K video streaming
  Remote office
  Cloud/edge computing
  Video calling and conferencing
Extremely High Throughput (EHT)
Operation in 2.4 GHz, 5 GHz, and 6 GHz bands
Higher throughout – Project goal of at least 30 Gbps; expect 40+Gbps with 320MHz channels, 4096 QAM
Support for low latency communications
Continued improvements in spectral efficiency
Targeted completion in 2024
January 2025
49

## Slide 50: 802.11be features under consideration
  Support of 320 MHz bandwidth channels, enabling extremely high throughput use cases
  More efficient utilization of non-contiguous spectrum
  Multi-band/multi-channel aggregation and operation
  MIMO protocol enhancements, enhanced sounding protocol
  Multi-AP Coordination (e.g. coordinated and joint transmission)
  Refinements of 802.11ax features: Multiple Resource Unit operation
  Target Wait Time (TWT) enhancements
  GCMP-256 support
  Adaptation to regulatory rules specific to 6 GHz spectrum
  NSEP priority access operation
January 2025

## Slide 51: The ARChitecture SC (ARC) meets on an ongoing basis
51
It does not develop a standard or amendment
Discussion of 802.11 architecture issues for other ongoing amendments
Topics for discussion include:
  Architectural clauses and models in the standard, as questions, or needs for update or clarification arise.
  Relationships with outside groups on 802.11 architectural topics, or topics that don’t fit elsewhere, such as IETF, 802 O&A, and 802.1.
January 2025

## Slide 52: ARC technical considerations
Models for STA architecture and related concepts, and overall system architecture, included in the Standard in clauses 4 and 5, generally.
Evolution of the models, either to consider amendments to the Standard, or as clarification is needed
Define how 802.11 technologies fit into 802, 802.1 and IETF use cases.
52
January 2025

## Slide 53: Thank You Questions
January 2025