## Slide 1
David Mazzarese (david.mazzarese@huawei.com)
Weiwei Fan (fanweiwei3@huawei.com)
Jiayin Zhang (zhangjiayin@huawei.com)
Mohamed Salem (Mohamed.Salem@huawei.com)
LBT for Short Control Messages
IEEE 802.11 Coexistence Workshop
Vienna, 17 July 2019

## Slide 2
Background
Channel access mechanisms for NR-U DRS
Evaluation assumptions, methodologies and results
Conclusions

## Slide 3
No LBT for transmission of short control signaling has been part of EN 301 893 for a long time
  Initially allowing up to 20% duty cycle, reduced to 5% duty cycle in v2.1.1 (suitable for LAA DRS and Wi-Fi)
  Proposals have been made to change “no LBT” to “short LBT” and to reduce from 5% to 1% duty cycle
  No LBT vs. Short (Cat2) LBT
  3GPP recognized that transmission of DRS in LAA can be relaxed to be pseudo-periodic without putting undue burden on UE implementations, which allows introducing Cat2 LBT before DRS transmission. Such behavior is further limited within DMTC windows (20 ms periodicity) and for DRS duration of at most 1 ms.
Maximum duty cycle
  Systems operating today in 5 GHz unlicensed bands use up to 5% duty cycle for short control signaling: LAA for DRS, and Wi-Fi for signaling to vacate the channel (as observed by Rhode & Schwarz at BRAN#102).
    Rohde&Schwarz observed Wi-Fi devices using Short Control Signalling Transmissions at >1%, typically between 1% and 5%. So according to Michael, limiting this to 1% would result in certain equipment already on the market not being compliant
Can anything be done better for the future?
  We start by looking at the impact of Cat2 LBT for the transmission of NR-U DRS
Background

## Slide 4
Current NR-U agreement on Channel access schemes for gNB as LBE device
  Scheme 1: always use Cat2 LBT within the DMTC only if DRS duration is up to 1 ms
    Allowing multiple Cat2 LBT attempts within the DMTC
Potential other channel access mechanisms for DRS
  Scheme 2: always use Cat4 LBT with high priority class with back off window [3,7]
    Probably limiting to a single attempt to transmit within the DMTC
  Scheme 3: DRS with Cat2 LBT and Cat4 LBT
    Allowing up to 5 Cat2 LBT in the DRS window. Cat4 LBT must be used for the other 15 DRS transmission occasions (within a 5 ms DRS window with 30 kHz subcarrier spacing)
  Scheme 4: DRS with hybrid Cat2/Cat4 LBT, completing Cat4 LBT as a condition for using Cat2 LBT with DMTC
    Allowing multiple Cat2 LBT attempts within the DMTC only after completing Cat4 LBT
Potential Access Mechanisms for DRS

## Slide 5
Figure 1 is the DRS success rate of the 4 cases/schemes in medium (BO = 40%) and high (BO = 60%) traffic load
  DRS transmission success rate = probability of LBT success for each attempt to transmit DRS within the DMTC
The results show some differences between the 4 cases of DRS success rate, the DRS success rate is more affected by Cat4 LBT compared to Cat2 LBT, especially in high traffic load.
Evaluations of DRS transmission success rate
Figure 1. DRS transmission success rate
(a) Medium load
(b) High load

## Slide 6
Evaluations of mean Wi-Fi beacon delay with average UPT of NRU and Wi-Fi under low/medium/high traffic loads
Table 1: High load | DL (Mbps) |  | UL (Mbps) |  | average beacon delay(ms)
 | Wi-Fi | NRU | Wi-Fi | NRU | 
Scheme 1 (DRS Cat2 LBT) | 37.00 | 45.27 | 33.64 | 34.56 | 9.4
Scheme 2 (DRS Cat4 LBT) | 36.24 | 44.38 | 32.83 | 32.94 | 9.0
Table 2: Medium load | DL (Mbps) |  | UL (Mbps) |  | average beacon delay(ms)
 | Wi-Fi | NRU | Wi-Fi | NRU | 
Scheme 1 (DRS Cat2 LBT) | 45.76 | 63.67 | 45.16 | 51.75 | 8.9
Scheme 2 (DRS Cat4 LBT) | 46.05 | 62.86 | 45.27 | 52.10 | 8.7
Table 3: Low load | DL (Mbps) |  | UL (Mbps) |  | average beacon delay(ms)
 | Wi-Fi | NRU | Wi-Fi | NRU | 
Scheme 1 (DRS Cat2 LBT) | 54.52 | 74.47 | 52.37 | 63.07 | 8.6
Scheme 2 (DRS Cat4 LBT) | 54.05 | 73.70 | 52.76 | 62.91 | 8.6
Note 1: in Wi-Fi/Wi-Fi coexistence, average beacon delay is 18.3/10.9/8.6 ms at high/medium/low load, respectively.
Note 2: The period of Wi-Fi beacon is 100ms. The NR-U DRS window periodicity is 20ms.

## Slide 7
How does DRS cope with varying traffic loads?
  In high traffic load DRS transmission with limited transmission attempts within a DMTC will be punished by Wi-Fi and other data, so the network will likely try and switch to a less loaded operating channel.
  In low load it should not be problematic to use up to 5% duty cycle with short LBT, although if many networks transmit DRS in uncoordinated manner then congestion could occur (see bullet #2 below). A network will likely switch to a less loaded operating channel once it is observed that CCA for DRS is frequently unsuccessful.
It has been argued that for standalone NR-U the use of short LBT for DRS signals with up to 5% duty cycle may be problematic if multiple gNBs operate asynchronously on the same channel.
  If alleviating congestion due to DRS only in dense NR-U networks is deemed problematic, solutions such as scheme 4 could be considered, which may also be beneficial in coexistence with Wi-Fi in extreme conditions.
It has been suggested that 3GPP should depart from the synchronized and scheduled nature of transmissions used for NR and LTE, including DRS. However 3GPP also considered constraints on implementations. It is beneficial for the 3GPP ecosystem to reuse UE implementations and mechanisms specified for RRM measurements and requirements in licensed bands.
Potential improvements to NR-U DRS channel access

## Slide 8
No significant difference in coexistence with Wi-Fi and in DRS success rate is observed by using Cat2 LBT or high-priority class Cat4 LBT for the channel access mechanism of NR-U DRS. The use of Cat2 LBT with a DMTC is considered beneficial for UE implementations.
More analysis would be required to determine whether a change of 3GPP agreement on DRS channel access mechanism (e.g. from Cat2 LBT to a hybrid of Cat2+Cat4 LBT) would be essential for future coexistence scenarios
Conclusions

## Slide 9
Annex: evaluation assumptions and methodology
Indoor scenario
Common configurations | 
Carrier Frequency | 6GHz
Carrier Channel Bandwidth | 20MHz baseline
Number of carriers | 1
Number of users per operator | Exactly 5 per gNB per 20MHz
Channel Model | Indoor: NR InH Mixed Office model for all links Outdoor:NR UMi street canyon for all links
BS/AP Tx Power | 23dBm (total across all TX antennas)
UE/STA Tx Power | 18dBm (total across all TX antennas)
BS/AP Antenna gain | 0 dBi
UE/STA Antenna gain | 0 dBi
BS/AP Noise Figure | 5dB
UE/STA Receiver Noise Figure | 9dB
UE receiver | MMSE-IRC
MIMO | DL/UL MU MIMO + DL/UL OFDMA, ideal CSI/CQI feedback
BS/AP antenna Array configuration | (M, N, P, Mg, Ng) = (1, 2, 2, 1, 1), dH = dV = 0.5 λ
UE/STA antenna Array configuration | Tx/Rx: (M, N, P, Mg, Ng) = (1, 1, 2, 1, 1), dH = dV = 0.5 λ
Traffic model | Use 36.889 Table A.1.1. Note: Results based on the mixed traffic models can be used to determine the design.
System specific configurations |  | 
 | NR-U | 802.11ax
Numerology | 60kHz SCS + ~1.2us CP for data 30kHz SCS for DRS (SSB) | 78.125kHz SCS + 0.8us CP
MCOT/TXOP | 8ms | 4ms
Response timing | K1 >= 0.75ms, K2 >= 0.75ms | 16us SIFS
Max MCS | NR LDPC with 256QAM | 802.11ac/ax LDPC with 256QAM
DMTC duration | 5 ms, with 0.25 ms shift for DRS | 
DRS | 1 ms duration, only transmitted with data if TXOP starts before DMTC | 
Other | CC-HARQ, 1 switching point within a COT. | MPDU: 1500B MSDU + 14 B header RTS/CTS off; NAV on MAC header

## Slide 10
Annex: UPT of DRS, DRS delay, and rate of partial DRS
Medium load | DL (Mbps) |  |  |  | UL (Mbps) |  |  |  | average DRS delay (ms) | probability of partial DRS
 | Wi-Fi (5%) | Wi-Fi (mean) | NRU (5%) | NRU (mean) | Wi-Fi (5%) | Wi-Fi (mean) | NRU (5%) | NRU (mean) |  | 
Scheme 1 | 13.15 | 46.05 | 21.14 | 64.91 | 8.96 | 41.1 | 13.76 | 49.63 | 2.25 | 1.14%
Scheme 2 | 12.9 | 45.82 | 21.94 | 65.28 | 9.12 | 41.17 | 13.34 | 49.63 | 2.63 | 1.22%
Scheme 3 | 12.77 | 45.98 | 21.17 | 65.17 | 9.55 | 41.71 | 13.16 | 49.38 | 2.57 | 1.04%
Scheme 4 | 12.77 | 46.12 | 20.6 | 64.8 | 8.46 | 40.71 | 13.29 | 49.19 | 2.26 | 1.23%
Table 1. UPT of DRS, DRS delay, and rate of partial DRS in medium traffic load (FTP3 λ=0.45, 40% buffer occupancy)
High load | DL (Mbps) |  |  |  | UL (Mbps) |  |  |  | average DRS delay (ms) | probability of partial DRS
 | Wi-Fi (5%) | Wi-Fi (mean) | NRU (5%) | NRU (mean) | Wi-Fi (5%) | Wi-Fi (mean) | NRU (5%) | NRU (mean) |  | 
Scheme 1 | 5.45 | 32.76 | 7.55 | 42.73 | 3.01 | 26.20 | 2.59 | 30.74 | 5.6 | 1.63%
Scheme 2 | 5.85 | 32.93 | 6.56 | 42.33 | 3.00 | 26.56 | 2.78 | 30.37 | 6.44 | 1.62%
Scheme 3 | 5.50 | 33.21 | 6.98 | 42.27 | 2.85 | 26.16 | 2.73 | 30.46 | 6.14 | 1.54%
Scheme 4 | 5.85 | 32.65 | 6.85 | 42.05 | 2.86 | 25.80 | 2.96 | 30.41 | 5.66 | 1.74%
Table 2. UPT of DRS, DRS delay, and rate of partial DRS in high traffic load (FTP3 λ=0.60, 60% buffer occupancy)
DRS delay = The time between the actually DRS transmission point and the starting point of DMTC, if LBT
failed in the DMTC, delay is counted as DRS period duration.
Note: DRS delay definition was corrected compared to v3 of this presentation