## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: UWB-IR (Impulse Radio) system proposed for the Low Rate alt-PHY (802.15.4a)
Date Submitted: Jan., 2005
Source: Benoit Miscopein (1), Patricia Martigne (2), Jean Schwoerer (3)
Company: France Telecom R&D
Address: 28 Chemin du Vieux Chêne – BP98 – 38243 Meylan Cedex - France
Voice: (1) +33 4 76 76 44 03, (2) +33 4 76 76 44 23, (3) +33 4 76 76 44 83
E-Mail: (1) benoit.miscopein@francetelecom.com, (2) patricia.martigne@francetelecom.com, (3) jean.schwoerer@francetelecom.com
Abstract: Complete proposal for 802.15.4a
Purpose: This document is a presentation of a complete proposal for the IEEE 802.15.4 alternate PHY standard
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15

## Slide 2: Contents
Structure of the UWB signal
Modulation, coding, multiple access technique
Spectrum aspects
PHY Frame Structure
System dimensioning
The transmitter
The antenna
The receiver
Ranging technique
Link Budget

## Slide 3: Structure of the UWB Signal
Impulse radio UWB :
* Very short pulses.
Each pulse (a wavelet) is about
1ns wide in time domain
<--> 1GHz bandwidth in frequency domain
* Pulses are transmitted within frames of Tf each
pulse-spacing = Tf ± TH
Pulse width = 1ns

## Slide 4: Modulation & coding
Bit to symbol mapping :
Binary (low speed mode) or quaternary (high speed) bit to symbol mapping.
Symbol-to-chip mapping :
Each symbol is a sequence of N chips.
Symbols are energy-equivalent.
2 (low speed) or 4 (high speed) orthogonal sequences available
OOK (On Off Keying) :
Chips are OOK-modulated
chip = '1'  a pulse is transmitted
chip = '0'  no pulse
Bit-to-Symbol
Symbol-to-Chip
OOK
Binary data from PPDU
Modulated signal

## Slide 5: Multiple access
Multiple access : TH (Time Hopping).
Each Symbol-time (Ts) is divided in N chip-time (Tc).
Each chip-time (Tc) is divided in M pulse-time (Tp).
A PN-code selects a pulse-time within the chip-time in which a pulse will be transmitted.
Each piconet has its own M-ary N-chip-long PN-code, selected in a set of nearly orthogonal sequences, and shared by all the members-devices.
Within the piconet :
Medium sharing is done via CSMA-CA (slotted if operating in beacon mode)

## Slide 6: Spectrum aspects
Bandwidth :
- At least 1GHz bandwidth (-3dB)
Center frequency : 2 options
- 4 GHz in the US and FCC-compliant country.
- 7 GHz to have easier worldwide regulatory compliance.
less potential (actual and future) interferer.
will cause less regulatory issues.

## Slide 7: Modulation, coding and multiple access
Example : if we choose :
- 8 pulse-time of 20 ns each.
- Tc = 8*20 = 160 ns chip period.
- TH code chip = 8-ary 8-sequence.
- 8 pulses transmitted for 1 symbol.
- 1 symbol = 1 bit (low speed mode).
This means :
=> a bit period of 8*160ns = 1280ns
=> PHY-SAP payload bit rate (Xo) = (1/(1280.10-9))*(1000/1024) = 763 kb/s

## Slide 8: PHY Frame Structure
Example of a standard PPDU data frame :
PHY Preamble sequence
PHY Header : Frame length
MAC Header : Frame control + Sequence nb + Addressing fields
MAC footer
4 bytes
1
PSDU : 32 bytes (e.g.)
2
1
8 (e.g.)
MSDU Data Payload
2
MPDU
The Start of Frame Delimiter is suppressed
it is replaced by a detection of bit-mapping modification (bit-mapping used for the preamble sequence will differ from the one used otherwise)
PPDU = 37 bytes for a 32-bytes standard PSDU

## Slide 9: Example of system dimensioning (1/5)
Example of a standard PPDU data frame
Data frame (37 bytes)
ACK
t ACK
LIFS
Next data frame
Time for an acknowledged transmission
Calculation of the useful rate for the standard 32-bytes PSDU, using "standard" speed (X0 = 763 kb/s) :
ttransmission = tdata-frame + tACK + tACK-frame + tLIFS = 560,64 µs
(considering 8 pulses/symbol, 1 symbol=1 bit, and tACK = 22 symbol-time)
This provides a useful rate of (32*8 bits / 560,64µs)*(1000/1024) = 446 kb/s
…

## Slide 10
Example of a standard PPDU data frame
For T0 = 1 kb/s (1024 bits/s),
this useful rate of 446 kb/s (corresponding to the transmission of 32 payload bytes i.e. 256 bits) means that the idle time for the system will be tidle = 249 msec approx.
Data frame
ACK
t ACK
LIFS
ttransmission
Transmission
N
Transmission
N+1
Transmission
N+2
Transmission
N+3
1024 bits in 1 sec
tidle
Example of system dimensioning (2/5)

## Slide 11
Example of a maximum PPDU data frame (127 bytes)
Calculation of the useful rate for the 127-bytes PSDU, using "high speed" mode (X1 = 1526 kb/s) :
In this mode, the mapping is made on 2 bit-symbols instead of being made on 1 bit-symbols for MSDU data payload bits, i.e. for (114 * 8) bits.
PPDU = (5 bytes)std-speed + (114 bytes)high-speed + (13 bytes)std-speed
tdata-frame = 768µs ttransmission = tdata-frame + tACK + tACK-frame + tLIFS = 949,76 µs
(considering 8 pulses/symbol, and tACK = 22 symbol-time)
This provides a useful rate of (127*8 bits / 949,76µs)*(1000/1024) = 1045 kb/s
Example of system dimensioning (3/5)

## Slide 12
For T1 = 500 kb/s (512 000 bits/s),
this useful rate of 1045 kb/s (corresponding to the transmission of 127 payload bytes i.e. 1016 bits) means that the idle time for the system will be tidle = 1 msec approx.
Data frame
ACK
t ACK
LIFS
ttransmission
Transmission
N
Transmission
N+1
Transmission
N+…
Transmission
N+503
512 064 bits in 1 sec
tidle
Example of system dimensioning (4/5)

## Slide 13
Fixing tidle = 250 µs (minimum required for CSMA-CA)
Example of system dimensioning (5/5)
Data frame
ACK
t ACK
LIFS
ttransmission
Transmission
N
Transmission
N+1
Transmission
N+…
Transmission
N+(x-1)
1 sec
tidle
Looking for the maximum aggregate channel throughput :
PSDU = 32 octets, std speed
  ttransmission = 560,64 µs
  x = 1234 transmitted packets
  Tmax-aggregate = 300 kb/s
PSDU = 127 octets, high speed
  ttransmission = 949,76 µs
  x = 834 transmitted packets
  Tmax-aggregate = 825 kb/s

## Slide 14: Contents
Structure of the UWB signal
Modulation, coding, multiple access technique
Spectrum aspects
PHY Frame Structure
System dimensioning
The transmitter
The antenna
The receiver
Ranging technique
Link Budget

## Slide 15: The transmitter
Pulse Generator
Clock
F < 100 MHz
Control Logic
BaseBand signal
RF Signal
PSDU Data
Guide Line : Keep it Simple
  Main Goal : "Low cost & low consumption".
  Pulses are generated in baseband.
  No mixer, no VCO but pulse shaping.
  Simple control logic and "reasonable" clock frequency (Crystal)
Pulse shaper
PA (option)

## Slide 16: Antenna characteristics
Frequency band: [3-10] GHz
Printed antenna 24x20 mm²
Omnidirectionnal radiation
Matching
2
4
10
6
8
GHz
SWR

## Slide 17: Antenna frequency response
Antenna gain
  @ 3 GHz: Gant= 4 to 5 dB
  @ 6 GHz: Gant= 3 dB
Due to antenna efficiency (printed antenna), in the budget link, we consider that Gant= 3 dB
3 GHz
6 GHz

## Slide 18: The receiver
One major guideline : Keep It Simple
Energy detection technique rather than coherent receiver, for relaxed synchronization constraints.
Threshold detection (no A/D conversion).
Synchronization fully re-acquired for each new packet received (=> no very accurate timebase needed).
Low cost, low complexity

## Slide 19: The receiver
x2
Lowpass filter
Threshold
Bandpass filter

## Slide 20: Packet Acquisition & Synchronisation
No sliding correlation.
PHY preamble sequence of 4 bytes with special bit mapping (all chips are set to 1).
Maximise preamble energy.
Every signal peak exceeding the treshold is acquired.
Triggers shall match arrival times defined by TH-Code.
Cost-effective synchronisation.
Synchronisation is fully re-acquired for each new packet
No need to maintain accurate timebase between packets.

## Slide 21: Packet Acquisition & Synchronisation
The synchronisation algorithm detects the threshold crossings and updates a assumption matrix, which can also be viewed as a tree exploration
i
Detected edge for t_pos(i)
i
No edge detection for t_pos(i)
?
2
3
4
3
4
Δ1,2
Δ2,3
Δ3,4
Δ2,3
Δ3,4
?
=
1
Time base origin determination
Δi,j = Known time offset between the pulses appearance, with respect to the TH code.

## Slide 22: Packet acquisition & Synchronisation
The threshold level is set to detect a number of crossings consistent with the expectations.
For any tested CM, the synchronisation is properly acquired (during the Synch header)
Measured accuracy is around several tens of ps.

## Slide 23: Performance simulations
Simulations done with a C++ simulator
TEB simulations performed only, each point obtained for 10 channel realisations.
One operating piconet simulations for CM1, CM2, CM3 and CM5
CM1 realisations do not provide any error in the simulated range

## Slide 24: Proposed ranging technique
Ranging capability based on the TOA/TWR technique
Ranging capabilities with fine precision :
system with an 1 GHz bandwidth, leading to an expected ranging accuracy of 30 cm.
Linked to the synchronisation acquisition organ, to detect the first path.

## Slide 25: Proposed ranging technique
Not yet fully tested.
Acquisition of a common time reference, thanks to 2 successive steps
  Short packets exchange (to get a first measurement)
  Requested device sends afterwards a Channel Sounding Frame (CSF), to refine the measurement (first path selection)
Can also be used for mutualised measurements, where the differents requesters can use the same CSF (e.g. inscription of a new device in the piconet), for free

## Slide 26: Proposed ranging technique
A
Request
ACK
Channel Sounding Frame
Z
Tw
T>Tg
B
Tw
ACK
Request
Tw
ACK
Request
N
t

## Slide 27: Energy Detection
ED uses exactly the same algorithm than synchronisation,
But it will run only with
1 byte of data instead of the 4-byte-packet preamble (which is twice more energetic than data)
About 9 dB less efficient than packet synchronisation.
Consistent with ED requirement for IEEE 802.15.4 (at most 10 dB above sensivity)

## Slide 28: Clear Channel Assessment
Introduction of a new value for the PhyCCAMode to allow a channel virtual listening operation (VLO) PhyCCAMode = 4
The CCA is made by Energy Detection (ED)
In beaconed or non beaconed systems, an active listening is processed at each Backoff period to get potentially addressed packets.
In PhyCCAMode = 4
  Signal detection and acquisition
  Decode the framelength byte, the ACKrequest bit and the adress fields to arm a VLO timer, including the Tack_max, if the packet is not addressed to the device
  In this case, any PLME-CCA.request leads to a PLME-CCA.confirm{BUSY}, during this time

## Slide 29: Clear Channel Assessment
Detection of a "competing" packet, by reading Framelength, ACKreq and address fields
Set a VLO vector =
Framelength+Tack_max+ACKlength (if needed)
PLME-CCA-request
BUSY
t
PLME-CCA-request
ED measure
Slot
Backoff period
ACK

## Slide 30: Clear Channel Assessment
Introduction of the VLO is valuable to lower the collision risks and the power consumption as TRX is shut down during VLO
The ED is performed by the signal acquisition organ : can discriminate
  Clear channel
  Intrapiconet activity : PLME-CCA.confirm{BUSY}
  Interpiconet interference : PLME-CCA.confirm{IDLE}

## Slide 32: Meeting the 802.15.4a objectives
Low cost system in terms of :
  Energy
  Financial aspect
  Technical complexity
use of a simple battery, with an autonomy of several years
use of a reasonable frequency clock (50 MHz)
8 pulses are transmitted per binary symbol, for redundancy and then robustness : very simple coding technique.