| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Text on Power Status Reporting Section for the IEEE 802.16m/D3 Amendment |
| Date Submitted | 2010-01-12 |
| Source(s) | Rongzhen Yang, Tim Wilson, Shi Liu, Joey Choi, Hujun Yin, Yang-seok Choi Intel Corp. and Motorola Yan-Xiu Zheng ITRI Jeongho Park Samsung Wookbong Lee LG Huiying Fang ZTE Corporation | Email: Rongzhen.yang@intel.com Email : Tim.Wilson@motorola.com E-mail: zhengyanxiu@itri.org.tw Email : jeongho.jh.park@samsung.com Email : wbong@lge.com E-mail: fang.huiying@zte.com.cn |
| Re: | Comments on P802.16m/D3 |
| Abstract | This contribution provides the proposed text for 16m uplink power status reporting. |
| Purpose | To be discussed and adopted into P802.16m/D3 |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed Text on Power Status Reporting Section for the IEEE 802.16m/D3 Amendment

Rongzhen Yang, Tim Wilson, Shi Liu, Joey Choi, Hujun Yin, Yang-seok Choi
Intel Corp. and Motorola

Yan-Xiu Zheng

ITRI

Jeongho Park

Samsung Electronics

Wookbong Lee

LG

Huiying Fang

ZTE Corporation

# Introduction

Power status reporting form AMS to ABS provides very important reference information for ABS uplink resource scheduling, which includes:

- Uplink power status definition;

- Uplink power status transmission conditions;

- Uplink power status reporting message design;

All those parts are missed in current 802.16m D3 amendment, in this contribution, the major parts of uplink power status reporting text are proposed.

# Key Reported Parameters

There are two key parameters for power status reporting: the base uplink transmission PSD and the  defined in section 16.3.9.4.1.

The base uplink transmission PSD is derived from equation (269) by setting  and :

The parameter is reported in dBm and is coded using 8 bits in 0.5 dBm steps ranging from -74 dBm (coded 0x00) to 53.5 dBm (coded 0xFF).

The reported value is coded using 10 bits in 1/16 dB steps ranging from -12dB (coded 0x000) to 51.9375 dB (coded 0x3ff).

After the ABS has received  and  from the AMS, the PSD for all uplink channels can be estimated in ABS.

For the range of reporting value, the  is easily derived and directly related to the AMS transmission power, so we discuss the range of  in the detail:

Firstly we can give some definitions for better expression:

The equation for  (equation 270) can be written as:

Note: the max[] part is omitted because it is not directly related to accuracy.

The derivative of y vs. x can be found to be:

To find the maximum value of we set  to its maximum ( =1) and  to its minimum. We can use y = -10dB and TNS=1, leading to a maximum value of of 11. This means that, worst-case, the quantization step of y is 11 times larger than the quantization step of x.

The problem then becomes finding a suitable range and quantization step size for reporting  that can represent  over a suitable range and resolution, for all possible values of , , and TNS.

The following figure shows the relation between  and for extreme values of , and TNS.=0 is not considered because in that case  is just SINR_min and the value of is not important.

Fig.1 The relationship of  and

From the figure it is clear that if the AMS reports db(SIR_DL) using 10 bits, in 1/16 dB steps over the range [-12 .. 51.9375] dB, then the ABS can derive the value of SINR_target over the range [-10 .. 35.9] dB with worst-case 0.6875 dB quantization, for all cases of , , and TNS.

# References

[1] IEEE P802.16m/D3, “Draft Amendment to IEEE Standard for Local and metropolitan area network: Air Interface for Fixed and Mobile Broadband Wireless Access Systems”, Oct. 2009.

# Text proposal

Instruction to editor;

Black text: existing D3 text

Blue and strike out text: for deletion

Red and underline text: for addition

[Remedy 1:]

[Insert one new subsection 16.3.9.4.6 “Uplink Power Status Reporting” after line 57 on the page 564, as follows:]

============================== Start of Proposed Text =================================

16.3.9.4.6 Uplink Power Status Reporting

16.3.9.4.6.1 Power Status Reporting Information

There are two key parameters for power status reporting: the base uplink transmission PSD and the  defined in section 16.3.9.4.1.

The base uplink transmission PSD is derived from equation (269) by setting  and :

(273)

The parameter is reported in dBm and is coded using 8 bits in 0.5 dBm steps ranging from -74 dBm (coded 0x00) to 53.5 dBm (coded 0xFF).

The reported value is coded using 10 bits in 1/16 dB steps ranging from -12dB (coded 0x000) to 51.9375 dB (coded 0x3ff).

After the ABS has received  and  from the AMS, the PSD for all uplink channels can be estimated in ABS.

16.3.9.4.6.2 Status Transmission Condition

The AMS shall send the status reporting message AAI_UL_PSR_Message to the ABS when the conditions listed below are met:

(274)

or

(275)

Where,

M is defined in equation 276:

(276)

Here, L is the pathloss defined in equation (269)

is data SINR target value calculated by equation (270)

is the frame index when the last AMS status reporting message was sent,.

is the current frame index.

txPowerReportThreshold is a 4 bit unsigned integer value in 0.5 dB steps, the specific value “0b1111” shall be interpreted as “infinite”;

txPowerReportMinimumInterval and txPowerReportPeriodicalInterval are coded by 4 bit unsigned integer values d representing frames, the specific value d=0b1111 shall be interpreted as “infinite”

The status reporting configuration parameters txPowerReportThreshold, txPowerReportMinimumInterval and txPowerReportPeriodicalInterval are sent from ABS to AMS in the message AAI-UL-PSR-CFG.

============================== End of Proposed Text =================================

[Remedy 2:]

[Insert the new text from line 44 on the page 117, under 16.2.3, as follows:]

============================== Start of Proposed Text =================================

16.2.3.xx Uplink Power Status Reporting Configuration (AAI-UL-PSR-CFG) message

An AAI-UL-PSR-CFG message is used to config the AMS uplink power status reporting by unicasting. It is defined as:

AAI-UL-PSR-CFG ::= SEQUENCE {

messageType		OCTET STRING (SIZE(1)),

uplinkPowerStatusReport		ENUMERATED {

disable (0),

enable (1)

},

-- Present when uplinkPowerStatusReport is enabled

psrReportConfigParameters		SEQUENCE {

txPowerReportThreshold          INTEGER (0..15),

txPowerReportMinimumInterval    INTEGER (0..15),

txPowerReportPeriodicalInterval    INTEGER (0..15)

} OPTIONAL

}

AAI-UL-PSR-CFG Field Descriptions

txPowerReportThreshold: txPowerReportThreshold is a 4 bit unsigned integer value in 0.5 dB steps, the specific value “0b1111” shall be interpreted as “infinite”

txPowerReportMinimumInterval: txPowerReportMinimumInterval is coded by 4 bit unsigned integer values d representing frames, the specific value d=0b1111 shall be interpreted as “infinite”

txPowerReportPeriodicalInterval: txPowerReportPeriodicalInterval is coded by 4 bit unsigned integer values d representing frames, the specific value d=0b1111 shall be interpreted as “infinite”

16.2.3.xx Uplink Power Status Report (AAI-UL-PSR) message

An AAI-UL-PSR message is used by the AMS to report uplink power status to ABS. It is defined as:

AAI-UL-PSR ::= SEQUENCE {

txPowerPsdBase			INTEGER (0..255),

txSirDownlink			INTEGER (0..1024)

}

AAI-UL-PSR Field Descriptions

txPowerPsdBase: txPowerPsdBase () is coded using 8 bits in 0.5 dBm steps ranging from -74 dBm (coded 0x00) to 53.5 dBm (coded 0xFF).

txSirDownlink: txSirDownlink () is coded using 10 bits in 1/16 dB steps ranging from -12dB (coded 0x000) to 51.9375 dB (coded 0x3ff).

============================== End of Proposed Text =================================

[Remedy 3:]

[Insert the new text from line 53 on the page 40, in 16.2.3, as follows:]

============================== Start of Proposed Text ==============================

| Message name | Message description | Security | Connection |
| --- | --- | --- | --- |
| AAI-UL-PSR -CFG | Uplink Power Status Reporting Configuration | Encrypted/ICV | Unicast |
| AAI-UL-PSR | Uplink Power Status Report | Encrypted/ICV | Unicast |

============================== End of Proposed Text ================================