| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | FEH Usage (16.2.2.2.1) |
| Date Submitted | 2010-07-09 |
| Source(s) | Anil Agiwal, Youngbin Chang, Rakesh Taori, Jungje Son Samsung Electronics | anilag@samsung.com, yb.chang@samsung.com, *<http://standards.ieee.org/faqs/affiliationFAQ.html |
| Re: | Sponsor Ballot on the Draft Amendment (IEEE P802.16m/D6). Topic: FEH (Section 16.2.2.2.1) |
| Abstract | This contribution clarifies the usage of FEH |
| Purpose | To be discussed and adopted by TGm for P802.16m/D7. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Copyright Policy | The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

FEH Usage

Anil Agiwal, Youngbin Chang, Rakesh Taori, Jungje Son

Samsung Electronics

# Introduction

In the IEEE P802.16m/D6 specification [1] it is defined that “The FEH shall also be included in the MAC PDU with AGMH if the transport connection payload in the MAC PDU contains an unfragmented MAC SDU which requires a sequence number.”

The meaning of 'Which require a Sequence number' is not clear in FEH description.

In case of unfragmented SDU in a MAC PDU, SN is required if the unfragmented SDU corresponds to an ARQ connection. For non ARQ connection, SN is required in case of unfragmented SDU for HARQ reordering as defined in section 16.2.4.4.1.1.

# Proposed text

[Modify the section 16.2.2.2.1, page 61, lines 24-30 as follows]

16.2.2.2.1 MAC SDU fragmentation extended header (FEH)

The FEH shall be included in the MAC PDU with SPMH/AGMH if the transport connection payload in the MAC PDU contains a fragment of MAC SDU. The FEH shall also be included in the MAC PDU with AGMH if the transport connection payload in the MAC PDU contains an unfragmented MAC SDU and either ARQ or MAC SDU inorder delivery is enabled for the transport connection which requires a sequence number. The FEH format is defined in Table 665.

# Reference

[1] IEEE P802.16m/D6, “DRAFT Amendment to IEEE Standard for Local and metropolitan area networks Part 16: Air Interface for Broadband Wireless Access Systems”