| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Moving stable ASN.1 code to section 16.2.3 |
| Date Submitted | 2010-09-15 |
| Source(s) | Joey Chou Intel Alessandro Triglia, Bancroft Scott OSS Nakalva Scott Probasco, Nokia | E-mail: joey.chou@intel.com sandro@oss.com baos@oss.com scott.probasco@nokia.com |
| Re: | TGm AWD: |
| Abstract | This contribution proposes text to Move stable ASN.1 code to section 16.2.3 |
| Purpose | Adopt proposed text. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

# Moving stable ASN.1 code to section 16.2.3

# Joey Chou,

# Intel

# Alessandro Triglia,

# Bancroft Scott

# OSS Nakalva

# Scott Probasco,

# Nokia

- Introduction

This contribution proposes to move stable ASN.1 code to section 16.2.3. The ASN.1 code without change marks are taken from Anenx R.2 of D8 draft. The ASN.1 code with change marks are the minor changes required to align with message tables in D8 draft.

- Proposed text

II.1 Proposed text 1

16.2.3 MAC Control messages

------------------------------------------------- Start of proposed Text --------------------------------------------------

[Editor Note: at Page 82, Line 56, add text as shown in the following, right after Table 678:]

The following lists the ASN.1 representation of MAC control messages as defined in Table 678.

MAC-Control-Message ::= SEQUENCE {

message               MAC-Control-Msg-Type,

...

}

MAC-Control-Msg-Type ::= CHOICE {

-- System information

aaiSCD                AAI-SCD,

aaiSIIAdv             AAI-SII-ADV,

aaiULPCNi             AAI-ULPC-NI,

-- Network entry / re-entry

aaiRngReq             AAI-RNG-REQ,

aaiRngRsp             AAI-RNG-RSP,

aaiRngAck             AAI-RNG-ACK,

aaiRngCfm             AAI-RNG-CFM,

aaiRegReq             AAI-REG-REQ,

aaiRegRsp             AAI-REG-RSP,

aaiSbcReq             AAI-SBC-REQ,

aaiSbcRsp             AAI-SBC-RSP,

-- Network exit

aaiDregReq            AAI-DREG-REQ,

aaiDregRsp            AAI-DREG-RSP,

-- Connection management

aaiDsaReq             AAI-DSA-REQ,

aaiDsaRsp             AAI-DSA-RSP,

aaiDsaAck             AAI-DSA-ACK,

aaiDscReq             AAI-DSC-REQ,

aaiDscRsp             AAI-DSC-RSP,

aaiDscAck             AAI-DSC-ACK,

aaiDsdReq             AAI-DSD-REQ,

aaiDsdRsp             AAI-DSD-RSP,

aaiGrpCfg             AAI-GRP-CFG,

-- Security

aaiPkmReq             AAI-PKM-REQ,

aaiPkmRsp             AAI-PKM-RSP,

-- ARQ

aaiArqFbk             AAI-ARQ-FBK,

aaiArqDsc             AAI-ARQ-DSC,

aaiArqRst             AAI-ARQ-RST,

-- Sleep mode

aaiSlpReq             AAI-SLP-REQ,

aaiSlpRsp             AAI-SLP-RSP,

aaiTrfInd             AAI-TRF-IND,

aaiTrfIndReq          AAI-TRF-IND-REQ,

aaiTrfIndRsp          AAI-TRF-IND-RSP,

-- Handover

aaiHoReq              AAI-HO-REQ,

aaiHoCmd              AAI-HO-CMD,

aaiHoInd              AAI-HO-IND,

aaiNbrAdv             AAI-NBR-ADV,

aaiNbrReq             AAI-NBR-REQ,

aaiScnReq             AAI-SCN-REQ,

aaiScnRsp             AAI-SCN-RSP,

aaiScnRep             AAI-SCN-REP,

-- Idle mode

aaiPagAdv             AAI-PAG-ADV,

aaiPgidInfo           AAI-PGID-INFO,

-- Multicarrier

aaiMcAdv              AAI-MC-ADV,

aaiMcReq              AAI-MC-REQ,

aaiMcRsp              AAI-MC-RSP,

aaiCmCmd              AAI-CM-CMD,

aaiCmInd              AAI-CM-IND,

aaiGlobalConfig       AAI-GLOBAL-CFG,

-- Power Control

aaiUlPowerAdj         AAI-UL-POWER-ADJ,

aaiUlPsrConfig        AAI-UL-PSR-CFG,

-- Collocated Coexistence

aaiClcReq             AAI-CLC-REQ,

aaiClcRsp             AAI-CLC-RSP,

-- MIMO

aaiSbsMimoFbk         AAI-SBS-MIMO-FBK,

aaiMbsMimoFbk         AAI-MBS-MIMO-FBK,

aaiDlIm               AAI-DL-IM,

aaiMbsMimoReq         AAI-MBS-MIMO-REQ,

aaiMbsMimoRsp         AAI-MBS-MIMO-RSP,

aaiMbsMimoSbp         AAI-MBS-MIMO-SBP,

aaiMbsSoundingCal     AAI-MBS-SOUNDING-CAL,

-- FFR

aaiFfrCmd             AAI-FFR-CMD,

aaiFfrRep             AAI-FFR-REP,

-- SON

aaiSonAdv             AAI-SON-ADV,

-- Relay

aaiARSCfgCmd          AAI-ARS-CFG-CMD,

-- EMBS

aaiEmbsCfg            AAI-EMBS-CFG,

aaiEmbsRep            AAI-EMBS-REP,

aaiEmbsRsp            AAI-EMBS-RSP,

-- LBS

aaiLbsAdv             AAI-LBS-ADV,

aaiLbsInd             AAI-LBS-IND,

-- Misc

aaiL2Xfer             AAI-L2-XFER,

aaiMsgAck             AAI-MSG-ACK,

aaiResCmd             AAI-RES-CMD}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.2 Proposed text 2

[Editor Note: at Page 81, Line 57, add text as shown in the following, befor section 16.2.3.1:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

The follwing lists the common type definitions that are used by MAC control messages.

-- *-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-

-- Common type definitions

-- *-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-

PhyCarrierIndex    ::= INTEGER (0..63)

LogCarrierIndex    ::= INTEGER (0..7)

PreambleIndex      ::= INTEGER (0..1023)

PreambleIndex2     ::= INTEGER (0..63)

PreambleIndex3     ::= INTEGER (0..127)

PCID               ::= BIT STRING (SIZE(48))

PGID               ::= BIT STRING (SIZE(16))

DREGID             ::= BIT STRING (SIZE(12))

PgCycle            ::= INTEGER (0..15)

PgOffset           ::= INTEGER (0..63)

PgOffset1          ::= INTEGER (0..4095)

FidChangeCount     ::= INTEGER (0..15)

AbsIndex           ::= INTEGER (0..255)

MBSZoneID          ::= INTEGER (0..127)

EMBSZoneID         ::= MBSZoneID

MacProtocolVersion ::= INTEGER (0..255)

BSID               ::= BIT STRING (SIZE(48))

STID               ::= BIT STRING (SIZE(12))

CID                ::= BIT STRING (SIZE(16))

FID                ::= INTEGER (0..15)

ReportMetric ::= BIT STRING {

absCINRMean (0),

absRSSIMean (1),

relativeDelay (2),

absRTD (3)} (SIZE(4))

RedirectionInfo ::= SEQUENCE {

absid                          BSID,

preambleIndex                  PreambleIndex,

centerFrequency                INTEGER(0..4294967295)}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.3 Proposed text

16.2.3.49 AAI-RES-CMD (Reset command)

------------------------------------------------- Start of proposed Text --------------------------------------------------

[Editor Note: at Page 233, Line 48, add text as shown in the following, right after Table 746:]

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Reset Command

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-RES-CMD ::= SEQUENCE {

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.4 Proposed text 4

16.2.3.36 AAI-MSG-ACK

------------------------------------------------- Start of proposed Text --------------------------------------------------

[Editor Note: at Page 184, Line 16, add text as shown in the following, right after Table 716:]

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- MAC Message Acknowledgement

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-MSG-ACK ::= SEQUENCE {

ackSN                          INTEGER (0..63),

cccid                          INTEGER (0..1),

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.5 Proposed text 5

16.2.3.30 L2 Transfer message (AAI-L2-XFER)

------------------------------------------------- Start of proposed Text --------------------------------------------------

[Editor Note: at Page 82, Line 56, add text as shown in the following, right after Table 678:]

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Layer 2 Transfer

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-L2-XFER ::= SEQUENCE {

transferType                   INTEGER {

gnssAssistance (1),

lbsMeasurement (2),

deviceBootstrap (3),

wirelessMAN (4),

oratMsg (5),

sms (6),

mihFrame (7),

relaySupport (8),

emergencyAlert (9)

} (0..255),

transferSubtype                INTEGER (0..15) OPTIONAL,

payload                        OCTET STRING (SIZE(1..9999))

OPTIONAL,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.6 Proposed text 6

16.2.3.19 AAI-FFR-CMD (FFR Command) Message

------------------------------------------------- Start of proposed Text --------------------------------------------------

[Editor Note: at Page 149, Line 37, add text as shown in the following, right after Table 699:]

-- *-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-

-- FFR Messages

-- *-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-

InterferenceMean ::= INTEGER (0..255)

InterferenceVariance ::= INTEGER (0..15)

SINRMean ::= INTEGER (0..255)

SINRVariance ::= INTEGER (0..15)

FFR-FeedbackIE ::= SEQUENCE {

interferenceMean               InterferenceMean OPTIONAL,

interferenceVariance           InterferenceVariance OPTIONAL,

sinrMean                       SINRMean OPTIONAL,

sinrVariance                   SINRVariance OPTIONAL

}

IntfStatistic ::= ENUMERATED {

noReportSent,

reportSent

}

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- FFR Measurement Report Command

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-FFR-CMD ::= SEQUENCE {

frequencyPartitionBitmap BIT STRING (SIZE(4)),

frequencyPartitionBitmap       SEQUENCE (SIZE(4)) OF IntfStatistic,

reportType                     BIT STRING {

interferenceMean (0),

interferenceVariance (1),

sinrMean (2),

sinrVariance (3)

} (SIZE(4)),

frameOffset                    INTEGER (0..255),

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.7 Proposed text 7

16.2.3.20 AAI-FFR-REP (FFR Report) Message

------------------------------------------------- Start of proposed Text --------------------------------------------------

[Editor Note: at Page 150, Line 65, add text as shown in the following, right after Table 700:]

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- FFR Measurement Report

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-FFR-REP ::= SEQUENCE {

frequencyPartitionBitmap       BIT STRING (SIZE(4)),

reportType                     BIT STRING {

interferenceMean (0),

interferenceVariance (1),

sinrMean (2),

sinrVariance (3)

} (SIZE(4)),

-- One report for each frequency partition.

-- A report is sent if the corresponding bit in

-- frequencyPartitionBitmap in AAI-FFR-CMD is set to reportSent

ffrReports                     SEQUENCE (SIZE(4)) OF SEQUENCE {

report                       FFR-FeedbackIE OPTIONAL

}, --one for each frequency partition

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.8 Proposed text 8

16.2.3.41 AAI-MULTI_BS_SOUNDING-CAL

------------------------------------------------- Start of proposed Text --------------------------------------------------

[Editor Note: at Page 191, Line 59, add text as shown in the following, right after Table 721:]

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Multi-BS Sounding Calibration

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-MBS-SOUNDING-CAL ::= SEQUENCE {

superframe                     ENUMERATED {

two,

four,

six,

eight},

frame                          INTEGER (0..3),

soundingAAISubframe            INTEGER (0..7),

soundingSubbandBitmap          BIT STRING (SIZE(0..24)),

decimationOffset               INTEGER (0..63),

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.9 Proposed text 9

16.2.3.40 AAI-MULTI_BS_MIMO-RSP

------------------------------------------------- Start of proposed Text --------------------------------------------------

[Editor Note: at Page 191, Line 22, add text as shown in the following, right after Table 720:]

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Multi-BS MIMO Response

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-MBS-MIMO-RSP ::= SEQUENCE {

adjABSBitmapMultiBSMIMO        BIT STRING (SIZE(8)),

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.10 Proposed text 10

16.2.3.39 AAI-MULTI_BS_MIMO-REQ

------------------------------------------------- Start of proposed Text --------------------------------------------------

[Editor Note: at Page 190, Line 56, add text as shown in the following, right after Table 719:]

MultiBSMIMORequestInfo ::= CHOICE {

singleBSPrecoding              SEQUENCE {

nipValueForSingleBS          INTEGER (0..3),

numberOfBSAboveThreshold     INTEGER (0..7),

tempBSID                     INTEGER (0..15)},

multiBSJointMIMOProcessing     SEQUENCE {

bitmapForRequestedAdjABSs    BIT STRING (SIZE(8)),

nipValueForJoint             INTEGER (0..3)

}

}

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Multi-BS MIMO Request

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-MBS-MIMO-REQ ::= SEQUENCE {

multiBSMIMORequest             MultiBSMIMORequestInfo,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.11 Proposed text 11

16.2.51 AAI-MC-REQ (multicarrier Request) Message

------------------------------------------------- Start of proposed Text --------------------------------------------------

[Editor Note: at Page 235, Line 58, add text as shown in the following, right after Table 748:]

FeatureSupport    ::= ENUMERATED {notSupported, supported}

McPhyCarrierIndex ::= INTEGER (0..15)

CarrierProc ::= SEQUENCE {

carriers                       SEQUENCE (SIZE(1..8)) OF

McPhyCarrierIndex,

dlULIndicator                  ENUMERATED {

bothDLAndUL,

dlOnly}

}

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- MultiCarrier Request

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-MC-REQ ::= SEQUENCE {

dataTxOverGuardCarrier         FeatureSupport,

multiCarrierProcess            CHOICE {

subsetOfCarriersSupported    NULLSEQUENCE (SIZE(0..3)) OF

CarrierProc,

allCarriersSupported         NULL SEQUENCE (SIZE(0..3)) OF

CarrierProc },

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.12 Proposed text 12

16.2.3.52 AAI-MC-RSP (multicarrier Respnse) Message

[Editor Note: at Page 236, Line 56, add text as shown in the following, right after Table 749:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

PhyCarrierIndex    ::= INTEGER (0..63)

AssignedCarrier ::= SEQUENCE {

carrierIndex                   PhyCarrierIndex,

dlULIndicator                  ENUMERATED {

bothDLAndUL,

dlOnly},

dataTxOverGuardCarrier         FeatureSupport

}

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- MultiCarrier Response

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-MC-RSP ::= SEQUENCE {

dataTxOverGuardCarrier FeatureSupport,

multiCarrierAssignment            CHOICE {

subsetOfCarriersAssignedSupported        NULL SEQUENCE (SIZE(1..8)) OF

AssignedCarrier,

allCarriersAssignedSupported              NULL CarrierProc

},

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.13 Proposed text 13

16.2.3.53 Carrier Management Command (AAI-CM-CMD) MAC control message

[Editor Note: at Page 240, Line 30, add text as shown in the following, right after Table 750:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

CarrierActivationInfo ::= SEQUENCE {

activationDeadline             INTEGER (0..63),

carrierInfoArray               SEQUENCE (SIZE(1..8)) OF SEQUENCE {

targetCarrier                McPhyCarrierIndex,

dlULActivated                ENUMERATED {

bothActivated,

dlOnlyActivated},

rangingIndicator             RangingIndicator}

}

CarrierDeactivationInfo ::= SEQUENCE {

carrierInfoArray               SEQUENCE (SIZE(1..8)) OF SEQUENCE {

targetCarrier                McPhyCarrierIndex,

dlULDeactivated              ENUMERATED {

bothDeactivated,

ulOnlyDeactivated}

}

}

RangingIndicator ::= ENUMERATED {

noRangingRequired,

periodicRangingRequired

}

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Carrier Management Command

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-CM-CMD ::= SEQUENCE {

carrierManagement              CHOICE {

secondaryCarrier             SEQUENCE {

activation                 CarrierActivationInfo OPTIONAL,

deactivation               CarrierDeactivationInfo OPTIONAL},

primaryCarrier               SEQUENCE {

carrierIndex               McPhyCarrierIndex,

actionTime                 INTEGER (0..7),

nextStateOfServCarrier     ENUMERATED {

deactivate,

keepActive},

rangingIndicator           RangingIndicator}

},

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.14 Proposed text 14

16.2.3.54 Carrier Management Indication (AAI-CM-IND) MAC control message

[Editor Note: at Page 240, Line 57, add text as shown in the following, right after Table 751:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Carrier Management Indication

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-CM-IND ::= SEQUENCE {

actionCode                     ENUMERATED {

secondaryCarrierChange,

primaryCarrierManagement},

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.15 Proposed text 15

16.2.3.33 AAI-UL_POWER_ADJ message

[Editor Note: at Page 180, Line 60, add text as shown in the following, right after Table 713:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

-- *-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-

-- Power Control Messages

-- *-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-

FeedbackControlInfo ::= SEQUENCE{

channelIndex                   INTEGER (0..255),

shortTermFeedbackPeriod        INTEGER (0..7),

longTermFeedbackPeriod         INTEGER (0..3),

frameOffsetNumber              INTEGER (0..3),

subframeIndex                  INTEGER (0..7),

allocationDuration             INTEGER (0..7)

}

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Uplink Transmit Power Adjustment

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-UL-POWER-ADJ ::= SEQUENCE {

offsetData                     INTEGER (0..63),

offsetControl                  INTEGER (0..63),

feedbackControlInfo            FeedbackControlInfo OPTIONAL,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.16 Proposed text 16

16.2.3.34 AAI-Uplink Power Status Reporting Configuration (AAI-UL PSR_Config) message

[Editor Note: at Page 181, Line 33, add text as shown in the following, right after Table 714:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Uplink Power Status Reporting Configuration

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-UL-PSR-CFG ::= SEQUENCE {

powerStatusReportConfig        SEQUENCE {

txPowerRptThreshold          INTEGER (0..15),

txPowerRptMinInterval        INTEGER (0..15),

txPowerRptPeriodicInterval   INTEGER (0..15)} OPTIONAL,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.17 Proposed text 17

16.2.3.17 AAI-CLC-REQ (Co-Located Coexistence Request)

[Editor Note: at Page 145, Line 53, add text as shown in the following, right after Table 696:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

-- *-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-

-- Collocated Coexistence Messages

-- *-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-

CLCID ::= INTEGER (0..7)

ClcRequest ::= SEQUENCE {

clcStartTime                   ClcStartTime,

schedulingImpact               ENUMERATED {

dlULProhibited,

dlProhibited,

ulProhibited

},

choice                         CHOICE {

typeI                        SEQUENCE {

startAAISubframeIndex      INTEGER (0..7),

activeInterval             INTEGER (0..255), -- No. of subframes

activeCycle                INTEGER (0..2097151) -- microseconds

},

typeII-1                     SEQUENCE {

activeBitmap               BIT STRING (SIZE(8))

},

typeII-2                     SEQUENCE {

startAAISubframeIndex      INTEGER (0..7),

activeInterval             INTEGER (0..255), --No. of subframes

activeCycle                INTEGER (0..255)  --No. of AAI frames

},

typeII-3                     SEQUENCE {

cycleLength                INTEGER(0..2),  -- No. of superframes

bitmap                     BIT STRING (SIZE(1..32))

},

typeIII                      SEQUENCE {

interval                   INTEGER (0..255)} -- no. of subframes

},

...

}

ClcStartTime ::= SEQUENCE {

clcId                 INTEGER (0..7),

startDfNumber         INTEGER (0..7), -- 3LSB of superframe number

startFrameIndex       INTEGER (0..3)}

ClcReportType ::= ENUMERATED {

coLocatedInterferenceLevel,

nonCoLocatedInterferenceLevel,

interferenceLevelSourceUnknown,

...

}

-- one bit for each CLC class (0=deactivate, 1=activate

ClcAction ::= BIT STRING (SIZE(1..8))

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Co-located Coexistence Request

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-CLC-REQ ::= SEQUENCE {

clcRequest            SEQUENCE {

requestAction       ClcAction,

clcRequest          SEQUENCE (SIZE(1..8)) OF ClcRequest OPTIONAL

} OPTIONAL,

clcReport             SEQUENCE {

reportType          ClcReportType,

interferenceLevel   INTEGER(-128..127) OPTIONAL

} OPTIONAL,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.18 Proposed text 18

16.2.3.18 AAI-CLC-RSP (Co-Located Coexistence Response)

[Editor Note: at Page 148, Line 9, add text as shown in the following, right after Table 697:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

ClcResponse ::= SEQUENCE {

confirmedAction         ClcAction,

clcStartTimes           SEQUENCE (SIZE(0..8)) OF ClcStartTime

}

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Co-located Coexistence Response

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-CLC-RSP ::= SEQUENCE {

clcResponse             ClcResponse,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.19 Proposed text 19

16.2.3.47.3 AAI-DSA-ACK

[Editor Note: at Page 220, Line 15, add text as shown in the following, right after Table 739:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

FidChangeCount     ::= INTEGER (0..15)

ConfirmationCode   ::= ENUMERATED {successful,

failure}

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- DSA Acknlowledge

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-DSA-ACK ::= SEQUENCE {

fidChangeCount                 FidChangeCount,

confirmationCode               ConfirmationCode

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.20 Proposed text 20

16.2.3.47.5 AAI-DSC-RSP

[Editor Note: at Page 229, Line 57, add text as shown in the following, right after Table 741:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

SFID               ::= BIT STRING (SIZE(32))

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- DSC Response

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-DSC-RSP ::= SEQUENCE {

fidChangeCount                 FidChangeCount,

sfid                           SFID OPTIONAL,

confirmationCode               ConfirmationCode,

groupParameterCreateChange     SEQUENCE {

fidList                      SEQUENCE (SIZE(1..8)) OF SEQUENCE {

fid                          INTEGER (0..15) OPTIONAL}

} OPTIONAL,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.21 Proposed text 21

16.2.3.47.6 AAI-DSC-ACK

[Editor Note: at Page 230, Line 18, add text as shown in the following, right after Table 742:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- DSC Acknlowledge

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-DSC-ACK ::= SEQUENCE {

fidChangeCount                 FidChangeCount,

confirmationCode               ConfirmationCode,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.22 Proposed text 22

16.2.3.47.7 AAI-DSD-REQ

[Editor Note: at Page 230, Line 1, add text as shown in the following, right after Table 743:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

EMBSID        ::= INTEGER(0..4095)

MBSZoneID     ::= INTEGER (0..127)

EMBSZoneID    ::= MBSZoneID

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- DSD Request

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-DSD-REQ ::= SEQUENCE {

fidChangeCount                 FidChangeCount,

fid                            FID OPTIONAL,

embsZoneID                     EMBSZoneID OPTIONAL,

embsidFIDMappingArray          SEQUENCE (SIZE(1..15)) OF SEQUENCE {

embsid                       EMBSID,

fid                          FID},

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.23 Proposed text 23

16.2.3.47.8 AAI-DSD-RSP

[Editor Note: at Page 231, Line 40, add text as shown in the following, right after Table 744:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- DSD Response

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-DSD-RSP ::= SEQUENCE {

fidChangeCount                 FidChangeCount,

sfid                           SFID OPTIONAL,

confirmationCode               ConfirmationCode,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.24 Proposed text 24

16.2.3.50 AAI-SII-ADV (Service Identity Information)

[Editor Note: at Page 234, Line 28, add text as shown in the following, right after Table 747:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

VerboseName ::= IA5String (SIZE(1..128))

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Service Identity Information Advertisement

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-SII-ADV ::= SEQUENCE {

nspInfoList                    SEQUENCE (SIZE(10..156)) OF NSPID,

verboseNspNameList             SEQUENCE (SIZE(10..156)) OF

VerboseName,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------

II.25 Proposed text 25

16.2.3.4 AAI-RNG-CFM

[Editor Note: at Page 99, Line 52, add text as shown in the following, right after Table 682:]

------------------------------------------------- Start of proposed Text --------------------------------------------------

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

-- Ranging Confirmation

-- +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-

AAI-RNG-CFM ::= SEQUENCE {

amsStid                        STID,

...

}

------------------------------------------------- End of proposed Text --------------------------------------------------