TD <>

ETSI EN 300 440-2 V1.2.1 (2007-05)

Candidate Harmonized European Standard (Telecommunications series)

Electromagnetic compatibility

and Radio spectrum Matters (ERM);

Short range devices;

Radio equipment to be used

in the 1 GHz to 40 GHz frequency range;

Part 2: Harmonized EN under article 3.2

of the R&TTE Directive

Reference

REN/ERM-TG28-0406-2

Keywords

radio, regulation, SRD, testing

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, send your comment to:
editor@etsi.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2007.

All rights reserved.

DECTTM, PLUGTESTSTM and UMTSTM are Trade Marks of ETSI registered for the benefit of its Members.
TIPHONTM and the TIPHON logo are Trade Marks currently being registered by ETSI for the benefit of its Members. 3GPPTM is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners.

Contents

Intellectual Property Rights	4

Foreword	4

Introduction	4

1	Scope	5

2	References	6

3	Definitions, symbols and abbreviations	6

3.1	Definitions	6

3.2	Symbols	6

3.3	Abbreviations	7

4	Technical requirements specifications	7

4.1	Environmental profile	7

4.2	Conformance requirements	7

4.2.1	Transmitter requirements	7

4.2.1	Equivalent isotropically radiated power	7

4.2.2	Permitted range of operating frequencies	7

4.2.3	Unwanted emissions in the spurious domain	7

4.2.4	Duty cycle	7

4.3	Receiver requirements	7

4.3.1	Adjacent channel selectivity	7

4.3.2	Blocking or desensitization	8

4.3.3	Spurious radiations	8

4.4	2,45 GHz RFID systems	8

4.4	GBSAR systems	8

5	Testing for compliance with technical requirements	8

5.1	Description of testing for compliance with technical requirements	8

5.1.1	Environmental conditions for testing	8

5.1.1.1	Normal and extreme test-conditions	8

5.1.1.2	Test power source	8

5.1.2	Choice of samples for test suites	8

5.2	Interpretation of the measurement results	9

5.3	Essential transmitter test suites	9

5.3.1	Equivalent isotropically radiated power	9

5.3.2	Permitted range of operation frequencies	9

5.3.3	Unwanted emissions in the spurious domain	9

5.4	Essential receiver test suites	10

5.4.1	Adjacent channel selectivity	10

5.4.2	Blocking or desensitization	10

5.4.3	Spurious radiations	10

5.5	Tests for RFID systems at 2.45 GHz	10

5.6	Tests for GBSAR systems	10

Annex A (normative): Harmonized Standard Requirements and conformance Test specifications Table (HS-RTT)	10

Annex B (informative): The EN title in the official languages	13

Annex C (informative): Bibliography	15

History	16

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://webapp.etsi.org/IPR/home.asp).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Candidate Harmonized European Standard (Telecommunications series) has been produced by ETSI Technical Committee Electromagnetic compatibility and Radio spectrum Matters (ERM).

The present document has been produced by ETSI in response to a mandate from the European Commission issued under Council Directive 98/34/EC  (as amended) laying down a procedure for the provision of information in the field of technical standards and regulations.

The present document is intended to become a Harmonized Standard, the reference of which will be published in the Official Journal of the European Communities referencing the Directive 1999/5/EC [1] of the European Parliament and of the Council of 9 March 1999 on radio equipment and telecommunications terminal equipment and the mutual recognition of their conformity ("the R&TTE Directive").

Technical specifications relevant to Directive 1999/5/EC are given in annex A.

The present document is part 2 of a multi-part deliverable covering Electromagnetic compatibility and Radio spectrum Matters (ERM); Short range devices; Radio equipment to be used in the 1 GHz to 40 GHz frequency range, as identified below:

Part 1:	"Technical characteristics and test methods";

Part 2:	"Harmonized EN under article 3.2 of the R&TTE Directive".

| National transposition dates |
| --- |
| Date of latest announcement of this EN (doa): | 3 months after ETSI publication |
| Date of latest publication of new National Standard or endorsement of this EN (dop/e): | 6 months after doa |
| Date of withdrawal of any conflicting National Standard (dow): | 18 months after doa |

# Introduction

The present document is part of a set of standards developed by ETSI and is designed to fit in a modular structure to cover all radio and telecommunications terminal equipment within the scope of the R&TTE Directive. The modular structure is shown in EG 201 399.

.

# 1	Scope

The present document applies to the following Short Range Device major equipment types:

Generic Short Range Devices, including alarms, identification systems, radio-determination, telecommand, telemetry etc ;

Radio Frequency IDentification (RFID);

Detecting and movement and alert applications.

These radio equipment types are capable of operating in the permitted frequency bands within the 1GHz to 40 GHz range as specified in table 1 below,

-	either with a Radio Frequency (RF) output connection and dedicated antenna or with an integral antenna;

-	for all types of modulation;

-	with or without speech.

Table 1 shows a list of the frequency bands as designated by the European Commission  Decision on Short Range Devices and the CEPT ERC Recommendation 70-03as known at the date of publication of the present Harmonized Standard.

# Table 1: Short Range Devices within the 1GHz – 40 GHz frequency band

|  | Frequency Bands | Applications | Notes |
| --- | --- | --- | --- |
| Transmit and Receive | 2400 MHz to 2483.5 MHz | Generic use |  |
| Transmit and Receive | 2400 MHz to 2483.5 MHz | Detecting and movement and alert applications |  |
| Transmit and Receive | (a) 2446 MHz to 2454 MHz | RFID | Note 1: See Annex C of EN 300 440-1 |
| Transmit and Receive | (b) 2446 MHz to 2454 MHz | RFID | Note 1: See Annex C of EN 300 440-1 |
| Transmit and Receive | 5725 MHz to 5875 MHz | Generic use |  |
| Transmit and Receive | 9200 MHz to 9500 MHz | Detecting and movement and alert applications |  |
| Transmit and Receive | 9500 MHz to 9975 MHz | Detecting and movement and alert applications |  |
| Transmit and Receive | 10.5 GHz to 10.6 GHz | For detecting and movement and alert applications |  |
| Transmit and Receive | 13.4 GHz to 14.0 GHz | Detecting and movement and alert applications |  |
| Transmit and Receive | 17.1GHz to 17.3 GHz | GBSAR detecting and movement and alert applications | Note 2: See Annex E of EN 300 440-1 |
| Transmit and Receive | 24.00 GHz to 24.25 GHz | Generic use and for detecting & movement & alert applications |  |

It should be noted that table 1 represents the most widely implemented position within the European Union and the CEPT countries, but it should not be assumed that all designated bands are available in all countries.

In addition, it should be noted that other frequency bands may be available in a country within the frequency range 1GHz to 40 GHz covered by this Harmonized Standard.

On non-harmonized parameters, national administrations may impose certain conditions such as the type of modulation, frequency, channel/frequency separations, maximum transmitter radiated power, duty cycle, and the inclusion of an automatic transmitter shut-off facility, as a condition for the issue of an individual or general licence, or as a condition for use under licence exemption

The present document covers fixed stations, mobile stations and portable stations. If a system includes transponders, these are measured together with the transmitter.

When selecting parameters for new SRDs, which may have inherent safety of human life implications, manufacturers and users should pay particular attention to the potential for interference from other systems operating in the same or adjacent bands.

Applications using Ultra- WideBand (UWB) technology are not covered by the present document.

The present document does not require measurements for radiated emissions below 25 MHz.

The present document is intended to cover the provisions of article 3.2 of Directive 1999/5/EC (R&TTE Directive) [1], see annex E of EN 300 440-1 [3].

In addition to the present document, other ENs that specify technical requirements in respect of essential requirements under other parts of article 3 of the R&TTE Directive [1] may apply to equipment within the scope of the present document.

NOTE:	A list of such ENs is included on the web site http://www.newapproach.org.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific.

For a specific reference, subsequent revisions do not apply.

For a non-specific reference, the latest version applies.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

[1]	. void

[2]	. void

[3]	ETSI EN 300 440-1 (V1.4.1): "Electromagnetic compatibility and Radio spectrum Matters (ERM); Short Range Devices (SRD); Radio equipment to be used in the 1 GHz to 40 GHz frequency range; Part 1: Technical characteristics and test methods".

[4]	 void

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in the R&TTE Directive and 
EN 300 440-1 [3] apply.

## 3.2	Symbols

For the purposes of the present document, the symbols defined in EN 300 440-1 [3] apply.

## 3.3	Abbreviations

For the purposes of the present document, the abbreviations defined in EN 300 440-1 [3] apply.

# 4	Technical requirements specifications

## 4.1	Environmental profile

The technical requirements of the present document apply under the environmental profile for operation of the equipment, which shall be declared by the supplier. The equipment shall comply with all the technical requirements of the present document at all times when operating within the boundary limits of the declared operational environmental profile.

## 4.2	Conformance requirements

## 4.2.1	Transmitter requirements

### 4.2.1	Equivalent isotropically radiated power

The equivalent isotropically radiated power, as defined in EN 300 440-1 [3], clause 7.1.1, shall not exceed the limits in 
EN 300 440-1 [3], clause 7.1.3, table 4.

This requirement applies to transmitters with an integral or dedicated antenna.

### 4.2.2	Permitted range of operating frequencies

The permitted range of operation frequencies, as defined in EN 300 440-1 [3], clause 7.2.1, shall not exceed the limits in EN 300 440-1 [3], clause 7.2.4.

### 4.2.3	Unwanted emissions in the spurious domain

The unwanted emissions in the spurious domain, as defined in EN 300 440-1 [3], clause 7.3.1, shall not exceed the limits in EN 300 440-1 [3], clause 7.3.7, table 6.

This requirement applies to all transmitters.

### 4.2.4	Duty cycle

The duty cycle, as defined in EN 300 440-1 [3], clause 7.4.1, shall not exceed the limits in EN 300 440-1 [3], clause 7.4.3, table 7.

This requirement applies to all transmitters.

## 4.3	Receiver requirements

### 4.3.1	Adjacent channel selectivity

The adjacent channel selectivity, as defined in EN 300 440-1 [3], clauses 8.1 and 8.1.1, shall not be less than the limits in EN 300 440-1 [3], clause 8.1.3, table 8.

This requirement applies to Equipment Category1 receivers, when invoked, as defined in EN 300 440-1 [3], clause 4.1.1.

### 4.3.2	Blocking or desensitization

The blocking or desensitization, as defined in EN 300 440-1 [3], clause 8.2.1, shall not be less than the limits in EN 300 440-1 [3], clause 8.2.3, table 10.

This requirement applies to Equipment Category1 and Category 2 receivers, when invoked, as defined in EN 300 440-1 [3], clause 4.1.1.

### 4.3.3	Spurious radiations

The spurious radiations, as defined in EN 300 440-1 [3], clause 8.3.1, shall not exceed the limits in
EN 300 440-1 [3], clause 8.3.5.

This requirement applies to all receivers.

## 4.4	2,45 GHz RFID systems

2,45 GHz RFID systems as defined in EN 300 440-1 [3], annex C, shall not exceed the limits as defined in
EN 300 440-1 [3], annex C, clauses C.1, C.1.1 and C.1.2.

## 4.4	GBSAR systems

GBSAR systems as defined in EN 300 440-1 [3], annex E, shall not exceed the limits as defined in EN 300 440-1 [3], annex E, clauses E.2.1, E.3.3.1, E.3.4.1.1, E.3.5.1, E.3.6.1 and E.3.7.1 shall not exceed the limits EN 300 440-1 [3], annex E clauses E.2.3, E.3.3.3, E.3.4.1.3, E.3.5.3, E.3.6.3 and E.3.7.3.

# 5	Testing for compliance with technical requirements

## 5.1	Description of testing for compliance with technical requirements

### 5.1.1	Environmental conditions for testing

Tests defined in the present document shall be carried out at representative points within the boundary limits of the declared operational environmental profile.

Where technical performance varies subject to environmental conditions, tests shall be carried out under a sufficient variety of environmental conditions (within the boundary limits of the declared operational environmental profile) to give confidence of compliance for the affected technical requirements.

#### 5.1.1.1	Normal and extreme test-conditions

The test procedures shall be as specified in EN 300 440-1 [3], clauses 5.3, and 5.4..

#### 5.1.1.2	Test power source

The test power source shall meet the requirements of EN 300 440-1 [3], clause 5.2.

### 5.1.2	Choice of samples for test suites

Measurement shall be performed, according to the present document, on samples of equipment defined in 
EN 300 440-1 [3], clauses 4.2.1 to 4.2.3.2.

## 5.2	Interpretation of the measurement results

The interpretation of the results recorded in a test report for the measurements described in the present document shall be as follows:

-	the measured value related to the corresponding limit will be used to decide whether an equipment meets the requirements of the present document;

-	the value of the measurement uncertainty for the measurement of each parameter shall be included in the test report;

-	the recorded value of the measurement uncertainty shall be, for each measurement, equal to or lower than the values in clause 10, table 11 of EN 300 440-1 [3]..

For the test methods, according to the present document, the measurement uncertainty figures shall be calculated in accordance with the principles contained within TR 100 028 (see bibliography) and shall correspond to an expansion factor (coverage factor) k = 1,96 or k = 2 (which provide confidence levels of respectively 95% and 95,45% in the case where the distributions characterising the actual measurement uncertainties are normal (Gaussian)).

The particular expansion factor used for the evaluation of the measurement uncertainty shall be stated.

### 5.3	Essential transmitter test suites

#### 5.3.1	Equivalent isotropically radiated power

Either:

the test specified in EN 300 440-1 [3], clauses 7.1.2 and 7.1.2.1 shall be carried out;

or

the test specified in EN 300 440-1 [3], clauses 7.1.2 and 7.1.2.2 shall be carried out.

This test suite applies to transmitters with an integral or dedicated antenna.

#### 5.3.2	Permitted range of operation frequencies

Either:

the test specified in EN 300 440-1 [3], clause 7.2.2 shall be carried out;

or

the test specified in EN 300 440-1 [3], clause 7.2.3 as appropriate shall be carried out.

This test suite applies to all transmitters.

#### 5.3.3	Unwanted emissions in the spurious domain

Either:

the tests specified in EN 300 440-1 [3], clause 7.3.3 and EN 300 440-1 [3], clause 7.3.4 shall be carried out;

or

the test specified in EN 300 440-1 [3], clause 7.3.5 shall be carried out.

This test suite applies to all transmitters.

### 5.4	Essential receiver test suites

### 5.4.1	Adjacent channel selectivity

the test specified in EN 300 440-1 [3], clause 8.1.2 shall be carried out.

This test suite applies to Category 1 and Category 2 receivers when invoked, as defined in EN 300 440-1 [3], clause 4.1.1.

.

### 5.4.2	Blocking or desensitization

the test specified in EN 300 440-1 [3], clause 8.2.2 shall be carried out.

This test suite applies to Category 1 and Category 2 receivers when invoked, as defined in EN 300 440-1 [3], clause 4.1.1..

### 5.4.3	Spurious radiations

Either:

the tests specified in EN 300 440-1 [3], clause 8.3.2 and EN 300 440-1 [3], clause 8.3.3 shall be carried out;

or

the test specified in EN 300 440-1 [3], clause 8.3.4 shall be carried out.

This test suite applies to all receivers.

## 5.5	Tests for RFID systems at 2.45 GHz

the test specified in clauses 5.3.1 and 5.3.2 shall be carried out.

## 5.6	Tests for GBSAR systems

the test specified in clauses 5.3.1 and 5.3.2 shall be carried out;

the test specified in EN 300 440-1 [3], clause 7.2 shall be carried out;

the test specified in EN 300 440-1 [3], Annex E, clauses E.3.3.2, E.3.4.1.2, E.3.5.2, E.3.6.2 and E.3.7.2 shall be carried out.

Annex A (normative):
Harmonized Standard Requirements and conformance Test specifications Table (HS-RTT)

The HS Requirements and conformance Test specifications Table (HS-RTT) in table A.1 serves a number of purposes, as follows:

it provides a statement of all the essential requirements in words and by cross reference to (a) specific clause(s) in the present document or to (a) specific clause(s) in a specific referenced document;

it provides a statement of all the test procedures corresponding to those essential requirements by cross reference to (a) specific clause(s) in the present document or to (a) specific clause(s) in specific referenced document(s);

it qualifies each requirement to be either:

Unconditional: meaning that the requirement applies in all circumstances, or

Conditional: meaning that the requirement is dependant on the manufacturer having chosen to support optional functionality defined within the schedule.

in the case of Conditional requirements, it associates the requirement with the particular optional service or functionality;

it qualifies each test procedure to be either:

Essential: meaning that it is included with the Essential Radio Test Suite and therefore the requirement shall be demonstrated to be met in accordance with the referenced procedures;

Other: meaning that the test procedure is illustrative but other means of demonstrating compliance with the requirement are permitted.

# Table A.1: HS Requirements and conformance Test specifications Table (HS-RTT)

| Harmonized Standard EN 300 440-2 The following essential requirements and test specifications are relevant to the presumption of conformity under Article 3.2 of the R&TTE Directive |
| --- |
| Essential Requirement | Requirement Conditionality | Test Specification |
| No | Description | Reference: Clause No | U/C | Condition | E/O | Reference: Clause No |
| 1 | Equivalent isotropically radiated power | 4.2.1 | U |  | E | 5.3.1 |
| 2 | Permitted range of operating frequencies | 4.2.2 | U |  | E | 5.3.2 |
| 3 | Unwanted emissions in the spurious domain | 4.2.3 | U |  | E | 5.3.4 |
| 4 | Duty cycle | 4.2.4 | C | Does apply for RFID in 1446 MHz to 1454 MHz only | X |  |
| 5 | Adjacent channel selectivity | 4.3.1 | C | Applies to Category 1 receivers only | E | 5.4.1 |
| 6 | Blocking or desensitization | 4.3.2 | C | Applies to Category 1 and Category 2 receivers | E | 5.4.2 |
| 7 | Spurious radiations | 4.3.3 | U |  | E | 5.4.3 |
| 8 | 2.45 GHz RFID systems | 4.4 | C | Applies to 2.45 GHz RFID systems only | E | 5.5 |
| 9 | GBSAR systems | 4.5 | C | Applies to GBSAR systems only | E | 5.6 |

Key to columns:

Essential Requirement:

No	A unique identifier for one row of the table which may be used to identify a requirement or its test specification.

Description	A textual reference to the requirement.

Clause Number	Identification of clause(s) defining the requirement in the present document unless another document is referenced explicitly.

Requirement Conditionality:

U/C	Indicates whether the requirement is to be unconditionally applicable (U) or is conditional upon the manufacturers claimed functionality of the equipment (C).

Condition	Explains the conditions when the requirement shall or shall not be applicable for a technical requirement which is classified "conditional".

Test Specification:

E/O	Indicates whether the test specification forms part of the Essential Radio Test Suite (E) or whether it is one of the Other Test Suite (O).

NOTE: 	All tests whether "E" or "O" are relevant to the requirements. Rows designated "E" collectively make up the Essential Radio Test Suite; those designated "O" make up the Other Test Suite; for those designated "X" there is no test specified corresponding to the requirement . The completion of all tests classified "E" as specified with satisfactory outcomes is a necessary condition for a presumption of conformity. Compliance with requirements associated with tests classified "O" or "X" is a necessary condition for presumption of conformity, although conformance with the requirement may be claimed by an equivalent test or by manufacturer's assertion supported by appropriate entries in the technical construction file.

Clause Number	Identification of clause(s) defining the test specification in the present document unless another document is referenced explicitly Where no test is specified (that is, where the previous field is "X") this field remains blank.

Annex B (informative):
The EN title in the official languages

| Language | EN title |
| --- | --- |
| Bulgarian |  |
| Czech | Elektromagnetická kompatibilita a rádiové spektrum (ERM) - Přístroje krátkého dosahu (SRD) - Rádiová zařízení pro použití v kmitočtovém rozsahu 1 GHz až 40 Hz - Část 2: Harmonizovaná EN pokrývající základní požadavky podle článku 3.2. Směrnice R&TTE |
| Danish | Elektromagnetisk kompatibilitet og spektrumanliggender (ERM) - Apparater med kort rækkevidde (SRD) - Radioudstyr som benytter frekvenser mellem 1 GHz og 40 GHz - Del 2: Harmoniseret EN, som dækker de væsentlige krav i R&TTE-direktivets artikel 3.2 |
| Dutch | Elektromagnetische compatibiliteit en radiospectrumzaken (ERM); apparatuur ten behoeve van korteafstandscommunicatie (SRD); radioapparatuur te gebruiken inde frequentieband van 1 GHz tot 40 GHz; deel 2: Geharmoniseerde EN om te voldoen aan de essentiële vereisten onder artikel 3, lid 2, van Richtlijn 1999/5/EG |
| English | Electromagnetic compatibility and Radio spectrum Matters (ERM); Short Range Devices (SRD); Radio equipment to be used in the 1 GHz to 40 GHz frequency range; Part 2: Harmonized EN covering essential requirements under article 3.2 of the R&TTE Directive |
| Estonian | Elektromagnetilise ühilduvuse ja raadiospektri küsimused (ERM); Lähitoimeseadmed (SRD); Raadiosagedusvahemikus1 GHz kuni 40 GHz; Osa 2: Harmoneeritud EN R&TTE direktiivi artikli 3.2 põhinõuete alusel |
| Finnish | Sähkömagneettinen yhteensopivuus ja radiospektriasiat (ERM); Lyhyen kantaman radiolaitteet (SRD); Taajuusalueella 1 GHz – 40 GHz toimivat radiolaitteet; Osa 2: Yhdenmukaistettu standardi (EN), joka kattaa R&TTE-direktiivin artiklan 3.2 mukaiset olennaiset vaatimukset |
| French | Télécommunications - Compatibilité radioélectrique et spectre radioélectrique (ERM) Appareils à faible portée - Equipements radioélectriques fonctionnant dans la gamme de fréquences de 1 GHz à 40 GHz. Partie 2 : paramètres non destinés à la procédure d'agrément |
| German | Elektromagnetische Verträglichkeit und Funkspektrumangelegenheiten (ERM) - Funkanlagen mit geringer Reichweite (SRD) - Funkgeräte zur Verwendung im Frequenzbereich von 1 GHz bis 40 GHz ;Teil 2: Harmonisierte EN, die wesentliche Anforderungen nach Artikel 3.2 der R&TTE-Richtlinie enthält |
| Greek | Ηλεκτρομαγνητική Συμβατότητα και Θέματα Ραδιοφάσματος (ERM) - Συσκευές μικρής εμβέλειας (SRD) – Ραδιοεξοπλισμός που προορίζεται να χρησιμοποιείται στην περιοχή συχνοτήτων 1 GHz ως 40 GHz -Μέρος 2: Εναρμονισμένο EN για την κάλυψη των ουσιωδών απαιτήσεων του Άρθρου 3.2 της Οδηγίας R&TTE |
| Hungarian | Elektromágneses összeférhetőségi és rádióspektrumügyek (ERM). Kis hatótávolságú eszközök (SRD). A 1 GHz – 40 GHz frekvenciasávban használt. 2. rész: Az R&TTE-irányelv 3.2. cikkelyének alapvető követelményeit tartalmazó, harmonizált európai szabvány |
| Icelandic | Þættir sem varða rafsegulsviðssamhæfi og fjarskiptatíðni (ERM); Skammdræg tæki (SRD): Fjarskiptabúnaður til nota á tíðnisviðinu 1 GHz til 40 GHz; Hluti 2: Samræmdur Evrópustaðall um grunnkröfur skv. 2. mgr. 3. gr. í tilskipun 1999/5/EC um fjarskiptabúnað og endabúnað til fjarskipta |
| Italian | Compatibilità elettromagnetica e spettro radio (ERM); Apparecchiature per comunicazioni a corto raggio (SRD); Apparati radio operanti nella banda di frequenza da 1 GHz a 40 GHz. Parte 2: Norma europea armonizzata relativa ai requisiti essenziali di cui all'articolo 3.2 della direttiva R & TTE |
| Latvian | Elektromagnētiskā saderība un radiofrekvenču spektra lietas. Maza darbības attāluma iekārtas. Radioiekārtas, ko izmanto frekvenču joslā no 1 GHz līdz 40 GHz. 2.daļa: Harmonizēts Eiropas standarts (EN), kas atbilst R&TTE Direktīvas 3.2.punkta būtiskām prasībām |
| Lithuanian | Elektromagnetinio suderinamumo ir radijo dažnių spektro dalykai. Mažojo nuotolio įranga. Radijo ryšio įranga, kuri naudojama nuo 1 GHz iki 40 GHz. 2 dalis. Darnusis Europos standartas, apimantis esminius reikalavimus pagal 1999/5/EC* direktyvos 3.2 straipsnį |
| Maltese | Kompatibilità elettromanjetika u materji relatati ma' spettru radjofoniku (ERM); Apparati ta' medda qasira; Tagħmir radjofoniku biex jintużaw fil-medda ta' frekwenzi 1 GHz sa 40 GHz; Parti 2: EN armonizzat li jkopri rekwiżiti essenzjali taħt l-artiklu 3.2 tad-Direttiva R&TTE |
| Norwegian | Elektromagnetisk kompatibilitet og Radiospektrum spørsmål (ERM); Kort distanse enhet (SRD); Radioutstyr som brukes i 1 GHz til 40 GHz området; Del 2: Harmonisert EN som dekker de vesentligste krav i R&TTE direktivets artikkel 3.2 |
| Polish | Kompatybilność elektromagnetyczna i zagadnienia widma radiowego (ERM ) -Urządzenia bliskiego zasięgu (SRD) - Urządzenia radiowe pracujące w zakresie częstotliwości 1 GHz do 40 GHz - Część 2: Zharmonizowana EN zapewniająca spełnienie zasadniczych wymagań zgodnie z artykułem 3.2 dyrektywy R&TTE |
| Portuguese | Assuntos de Espectro Radioeléctrico e Compatibilidade Electromagnética (ERM); Equipamento de curto alcance (SRD); Equipamento de rádio com, para a faixa de frequências de 1 GHz a 40 GHz ; Parte 2: EN harmonizada cobrindo os requisitos essenciais no âmbito do artigo 3º, nº 2, da Directiva R&TTE |
| Romanian |  |
| Slovak | Elektromagnetická kompatibilita a záležitosti rádiového spektra (ERM). Zariadenia s krátkym dosahom (SRD). Rádiové zariadenia používané vo frekvenčnom rozsahu od 1 GHz do 40 GHz s úrovňami. Časť 2: Harmonizovaná EN vzťahujúca sa na základné požiadavky podľa článku 3.2 smernice R&TTE |
| Slovenian | Elektromagnetna združljivost in zadeve v zvezi z radijskim spektrom (ERM) - Naprave kratkega dosega (SRD) - Radijska oprema, ki se uporablja v frekvenčnem območju od 1 GHz do 40 GHz – 2. del: Harmonizirani EN, ki zajema bistvene zahteve člena 3.2 direktive R&TTE |
| Spanish |  |
| Swedish | Elektromagnetisk kompatibilitet och radiospektrumfrågor (ERM); Kortdistansutrustningar (SRD); Radioutrustning för användning i frekvensområdet 1 GHz till 40 GHz; Del 2: Harmoniserad EN omfattande väsentliga krav enligt artikel 3.2 i R&TTE-direktivet |

Annex C (informative):
Bibliography

ETSI EG 201 399 (V2.1.1): "Electromagnetic compatibility and Radio spectrum Matters (ERM); A guide to the production of candidate Harmonized Standards for application under the R&TTE Directive".

ETSI TR 100 028 v.1.4.1 (2001-12) (all parts): "Electromagnetic compatibility and Radio spectrum Matters (ERM); Uncertainties in the measurement of mobile radio equipment characteristics".

Directive 1999/5/EC of the European Parliament and of the Council of 9 March 1999 on radio equipment and telecommunications terminal equipment and the mutual recognition of their conformity (R&TTE Directive)

Directive 98/34/EC of the European Parliament and of the Council of 22 June 1998 laying down a procedure for the provision of information in the field of technical standards and regulations

CEPT/ERC Recommendation 70-03 (2007): "Relating to the use of Short Range Devices (SRD)"

History

| Document history |
| --- |
| V1.1.1 | September 2001 | Publication |
| V1.1.2 | July 2004 | Publication |
| V.1.2.1 | May 2007 | 1st draft ETSI TG28#17bis output |