## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-05-0408-01-0000
Title: IETF Involvement on Higher layer Information Service
Date Submitted, January 2005
Authors or Source(s):
  Subir Das, Srinivas Sreemanthula, Yoshihiro Ohba, Ajoy Singh, Kalyan.koora, Wolfgang Groeting, Kenichi Taniuchi, Stefano Faccin
  Abstract: This document provides few options regarding IETF involvement in IEEE 802.21 Information Service work. The purpose of this proposal is to discuss these options within the group and to decide a single option that fits best to IEEE 802.21 higher layer Information Service.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>

## Slide 3: Background
During October 25, 2005, teleconference, 802.21 members have discussed the IS requirements
The group has felt a need to clearly identify the role that IETF can play in defining the Information Service
  The MIH IS components are Information Elements (IEs), MIH Protocol and MIH Transport
Several options were discussed and are captured in next couple of slides
The purpose of this exercise is to get a consensus on a single option that fits best for IEEE 802.21 and then create appropriate IETF requirements

## Slide 4: Terminology
MIH Information Elements (MIH-IE)
  Every MIH-IE is represented as MIH-IE header and MIH-IE Data
MIH Payload
  MIH payload consists of MIH-IEs, ….
MIH Packet / MIH Protocol
  MIH-Packet consists of MIH-Header and MIH Payload
MIH Transport
  MIH Transport carries MIH packets/protocol from one MIHF peer to the other
  Transport Protocol consists of transport header and transport IEs

## Slide 5: Option Ia
Transport Payload
Transport
Header
MIH Payload
MIH
Header
MIH IE Header
MIH IE Data
IE1
IE2
IEn
MIH IE Header
MIH IE Header
MIH IE Data
MIH IE Data
IETF 
IEEE 
IEEE 
IEEE defines and specifies MIH protocol exchange, MIH Protocol Header and Payload (MIH IE header and data).
IETF defines and specifies the Transport Header and also the Transport protocol

## Slide 6: Option 1b
Transport Payload (IETF)
Transport
Header
MIH Payload
MIH
Header
MIH IE
Data
Container Protocol Header
MIH IE
Header
MIH IE
Header
MIH IE
Data
IEn
IETF 
IETF 
IE Header
IE1
Transport Payload (IEEE)
MIH IE
Data
IE
Data
MIH IE
Header
MIH IE
Data
MIH IE Header
IEEE 
IEEE 
IE Header
IE
Data
IE1 (IETF)
IEn (IETF)
Transport Payload (IEEE)
IEEE defines and specifies MIH protocol exchange, MIH Protocol Header and Payload (MIH IE header and data).
IETF defines and specifies the Transport Header and a container protocol header and related IE
IE2

## Slide 7: Option 2
IE1
IE2
IEn
Transport Payload
Transport
Header
MIH Payload
MIH
Header
MIH IE Header
MIH IE Data
MIH IE Header
MIH IE Header
MIH IE Data
MIH IE Data
IEEE 
IETF
IEEE
IETF 
IEEE defines and specifies MIH protocol exchange, MIH message types and MIH payload (MIH IE hdr and Data)
IEEE defines MIH header (including message types) and provides it to IETF
IETF defines and specifies the Transport Header
IETF specifies the MIH header
  For any new functionality (based on requirements) will require definition and specification

## Slide 8: Option 3a
Transport
Header
MIH Payload (IETF)
MIH
Header
MIH IE Header
MIH IE Data
IE2
IEn
MIH IE Header
MIH IE Data
IETF
IETF
IEEE
IEEE
IETF 
IEEE defines and specifies MIH protocol exchange, message types and IEEE related MIH IE payload (MIH IE header and data)
IEEE defines MIH header (including the message types) and provides it to IETF
IETF defines and specifies the Transport Header
IETF specifies the MIH header
  For any new functionality (based on requirements) will require definition and specification
IETF defines and specifies IETF related MIH IE payload
MIH Payload (IEEE)
IETF
MIH IE Header
MIH IE Data
MIH IE Header
MIH IE Data
IE2
IEn
Transport Payload (IETF)
Transport Payload (IEEE)

## Slide 9: Option 3b
Transport
Header
MIH
Header
MIH IE Data
IE Container1
Container Header
MIH
IE Header
Container Header
MIH IE Data
MIH IE Header
IE Container n
IETF
IETF
IEEE
IETF
IETF 
MIH IE Data
MIH IE Header
Same as 3a
Additionally, IETF defines and specifies a container header (to carry different kinds of payload)
MIH IE Data
MIH
IE Header
MIH Payload (IETF)
IEEE
MIH Payload (IEEE)
IETF
Transport Payload (IETF)
Transport Payload (IEEE)

## Slide 10: Conclusions to date
Based on discussion on Dec. 8, 2005
Options 1a and 3a are more likely to succeed with IETF, since they enable cooperation and open dialogue with IETF, wrt just asking them for a transport of a “close” protocol defined in IEEE. 3a would force more cooperation and open dialogue.
However, another possibility emerged  option 3c

## Slide 11
Option 3c
What: an option to maintain the logic of the MIH protocol defined in 802.21 while allowing for flexibility for IETF
Why:
  With option 3a we would allow IETF to work together with 802.21 and add IEs needed for IETF and needed to provide a complete functionality (e.g. security IEs to secure 802.21 protocol).
    However, 3a implies the MIH header is defined by IETF, and this may impact the logic of the MIH protocol defined by 802.21.
  There seem to be agreement that 802.21 shall define its own IEs, the MIH header and the related protocol logic, while allowing IETF to extend the list of IEs and perhaps add functionality to the protocol
    This would allow for a more cooperative approach with IETF and not be perceived as pure rubberstamping
    This would also allow for valuable input from IETF
How: option 3c is a slight modification of option 3a (can be considered a clarification of 3a):
  IEEE defines and specifies MIH protocol exchange (logic of the protocol), message types and IEEE related MIH IE payload (MIH IE header and MIH IE data)
  IEEE initially defines MIH header (including the message types) for IS, ES and CS (may be a single header for all) and provides it to IETF
  IEEE collaborates with IETF in finalizing the header.
    This allows IETF to add information to the header to “complete” it based on requirements (e.g. add security-specific fields)
    This option allows IETF to define other headers besides the one(s) defined by/with IEEE. Such headers are not related to MIH services
  IETF defines and specifies IETF-related MIH IE payload: this can be e.g. IEs for securing the MIH protocol in case of L3 transport (according to security mechanisms defined in IETF)
  IETF defines and specifies the Transport Header
MIH
Header
Transport
Header
MIH Payload (IETF)
MIH IE Header
MIH IE Data
IE2
IEn
MIH IE Header
MIH IE Data
IETF
IETF
IEEE
IEEE
IETF 
MIH Payload (IEEE)
IETF
MIH IE Header
MIH IE Data
MIH IE Header
MIH IE Data
IE2
IEn
Transport Payload (IETF)
Transport Payload (IEEE)
MIH
Header
who is the
consumer of
IETF-MIH IEs?

## Slide 12: Clear Division of Work
IEEE 802.21
MIH-Packet
(=MIH-Header+MIH-Payload)
IETF
IETF MIH-Packet
(=IEEE MIH-Packet + ???)
Peer 1
IEEE 802.21
MIH-Packet
(=MIH-Header+MIH-Payload)
IETF
IETF MIH-Packet
(=IEEE MIH-Packet + ???)
Peer 2
L3 Transport
Exchange of
MIH-Packet as
defined by IEEE
Exchange of
IETF MIH-Packet as
defined by IETF
Exchange of
MIH-Packet as
defined by IEEE
Adapter
Adapter
Adapter:
at Tx, takes MIH-Packets as defined by IEEE from MIHF & converts them into IETF MIH packets either with option 1a/1b/3c/??
at Rx, takes IETF MIH packets and converts them into MIH packets as defined by IEEE and delivers it to MIHF (consumer)
may have the capability to exchange IP packets between peers or hand the packets to some OS specific IP stack for transport
is then to be defined by IETF (may be in co-operative work with IEEE, how?)
is not in scope of IEEE 802.21
Asumption: seen from IEEE 802.21 point of view