## Slide 1: EFM OAM Coding Violation Counters Ben Brown – AMCC

## Slide 2: Coding Violation Counters
1000BASE-X
  Define a new 8B/10B coding violation counter that increments for all INVALID code-groups based on the running disparity rules and Tables 36-1 & 36-2
  16-bit counter supports a BER of 5x10-4 without reaching a max value in 1 sec – 65535 / (125x106) = 5.24x10-4 – granularity is 10 bits
100BASE-X
  Define a new 4B/5B coding violation counter that increments for all INVALID code-groups, other than /H/, as defined in Table 24-1
  16-bit counter supports a BER of 2.6x10-3 without reaching a max value in 1 sec – 65535 / (25x106) = 2.62x10-3 – granularity is 5 bits

## Slide 3: Applications
Access counters directly
  Used by upper layer applications and directed tests
  X BER for Y time requires Z counter bits (see previous slide)
Provide thresholds & alarms
  Eliminates polling by upper layer applications
  Ideal to detect
    Errored Seconds (ES – a second with >= 1 violation)
    Severely Errored Seconds (SES – a second with >= X violations)
  Even better to track these over many seconds
    Alarm after Y Errored Seconds or Z Severely Errored Seconds

## Slide 4: What gets spec’ed?
The dilemma is how much to standardize
Need to add the 2 counters but how wide?
Add a threshold to look for SES?
Add an ES & SES alarms?
Add counters to count ES & SES?
Add ES & SES counter thresholds to generate alarms?

## Slide 5: Recommendation
In D1.1, only add Coding Violation Counters
Request comments and associated presentations to add supporting logic